## Slide 1: Design Concepts with System Architect: Level 0
John Leidel
Chief Scientist, Tactical Computing Laboratories
ver 2012.09.13

## Slide 2: Tutorial Series
Level 0: Introduction to System Architect
Level 1: System Architect Design Concepts and Developing a basic RISC processor
Level 2: Instruction-Level (StoneCutter) Implementation Concepts
Level 3: Advanced Design Concepts
Level 4: System Architect Plugins and Integrating External RTL

## Slide 3: System Architect Overview
Modular, High-Level Design Concepts

## Slide 4: What is System Architect?
A family of tools, APIs and associated infrastructure to permit users to rapidly develop multi-faceted hardware
Utilizes a combination of modular hardware design reuse principles, object oriented development and dependence analysis techniques (compiler theory) to provide an infrastructure for:
  Design & Design Experimentation
  High Level Verification
The artifacts generated by a System Architect design flow include:
  Chisel HDL and Verilog RTL
  C++ cycle-based simulator
  LLVM compiler

## Slide 5: What is System Architect NOT?
System Architect is not the latest C-to-gates tool
  It permits rapid design, verification and reuse
  It does not auto-generate hardware based upon application code
System Architect still relies upon the user to utilize reasonable design concepts
  System Architect will not auto-generate optimized designs based upon unreasonable inputs
  Users need to have a concept of the physical platform (FPGA, ASIC, etc)
System Architect does not currently have a notion of physical layout
  The generated output will not include LUT counts, physical design dimensions or power estimates
  External FPGA/ASIC tools are required for this level of detail

## Slide 6: System Architect Design Flow
Design Input
IR
Verification
Code Generation
Chisel HDL
LLVM Compiler
Verilog
C++ Simulator
User
The user inputs their design using the GUI or text editor. This includes the design parameters and logic for each instruction
The design input is stored in the CoreGen intermediate representation (IR)
The user then executes verification passes against the design in order to ensure the design is correct and optimal. Users have the option of executing special passes to generate design documentation
The user executes the codegen in order to generate the Chisel HDL and/or the LLVM compiler for the target design
The user an now optionally utilize the Chisel HDL to generate the Verilog representation and the C++ simulator. The LLVM compiler can be utilized to drive binary payloads for the C++ simulator
Verilog output can be utilized for downstream synthesis and layout tools

## Slide 7: Typical System Architect Design Flows
Rapid ISA Development
Rapid development of ISA’s with backend RTL and LLVM compiler as artifacts
Cycle-based simulator that supports immediate experimentation
Rapid design evaluation and prototyping
High level verification of design before synthesis
Modular Design
Multi-module design and integration
Integration with other System Architect designs (sub-designs)
External module integration
Plugin support for custom-modularity
Compiler Environment
Auto-generated LLVM compiler infrastructure from design parameters
Modern C/C++ frontend support
  Other frontends can be supported as well
Re-useable as LLVM mainline continues to develop
  Re-spinning entire compiler based on new LLVM versions is automated

## Slide 8: System Architect Infrastructure
CGCLI
Command Line Interface
User Interfaces
CoreGen Infrastructure
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
StoneCutter Compiler
SC Input
SC Input
SC Input
SC Input
SC Input
SC Input
CodeGen
LLVM Source Compiler
Chisel HDL
Backend Infrastructure
YAML
IR
Verilog
C++ Cycle Sim

## Slide 9: How does it work?
We input designs in the user-facing tools and generate CoreGen Intermediate Representation (IR)
The IR preserves the natural dependencies within the design
  Register classes depend upon registers
  Instruction formats depend upon register classes
  Instruction sets depend upon instructions
  Cores require instruction sets
We execute high level verification “passes” against the IR
  Similar in design to traditional compiler passes
  Walks the IR dependence graph and derives properties of the design
  Reports issues in the design infrastructure, outputs interesting data or optimizes the design infrastructure
Users implement instructions in StoneCutter instruction implementation language
  C-like integrated with CoreGen IR to define a single instruction
  Optimized by a traditional compiler flow to generate Chisel HDL for a single instruction
Following the high level verification phase, we execute generate downstream code (code generation)
  Generates Chisel HDL
    Compiled down to Verilog & C++ cycle-based simulator
  Generates LLVM compiler for the target design
Example dependence graph from CoreGen design input

## Slide 10: CoreGen IR Passes
Passes can be selectively enabled or disabled by the user (just like a normal compiler)
Four types of passes
  Analysis
    Analyze the connectivity and the structure of the graph
    Reports back the identified state to the user
    DOES NOT modify the graph (IR is unchanged)
  Optimization
    Optimizes connectivity and structure of the graph
    Much like Kennedy/Callahan dependence analysis/optimization
    MODIFIES the dependence graph (IR is changed)
  Data
    Generates statistical data/output based upon the structure/content of the graph
    EG, outputs a LaTeX specification document based upon the respective ISA
    DOES NOT modify the graph (IR is unchanged)
  System
    Mixtures of each of the aforementioned pass types
    Must be manually instantiated by the tools/users
The internal representation of the IR is stored as a directed acyclic graph (DAG)
Contains four levels that describe varying levels of detail
  This is a performance optimization
  Each subsequent level is a superset of the previous level

## Slide 11: CoreGen IR Passes: Example Analysis Passes
RegSafetyPass/RegIdxPass
Find inconsistencies between registers within the same register file
Multiple registers with the same index
Registers with missing indicies
Registers with prescribed values > than their bit width
Sub-register fields with overlapping names
Sub-register fields with overlapping bit field definitions
EncodingCollisionPass
Identifies potential ISA encoding issues
Utilizes all instruction formats within an ISA
Builds a table of every known instruction within the ISA
  Initializes a bit vector for every instruction using the encoding (eg, opcode), immediate values and register fields (bitmask)
Examines collisions in the “loaded” encodings

## Slide 12: CoreGen IR Passes: Example Data Passes
StatsPass
Walks the entire dependence graph and collects data about the connectivity of the graph and incidence of the nodes
Reports the number of adjacent dependent nodes for each node in the graph (outdegree)
Reports final counts of the incidence of each node type
SpecDoc
Walks the entire dependence graph and collects data about the encoding infrastructure of the ISA and portions of the micro architecture
Outputs a specification document in LaTeX that details each of:
  Register Classes
  Register Encodings
    Subregister encodings (bit fields within register)
  Instruction Formats
  Instruction Encodings
  Master instruction table

## Slide 13: CoreGen IR Passes: Example System Passes
SafeDeletePass
Determines whether removing a node from the graph is safe
For example:
  ”If I remove this register, will I break the dependence graph?”
  “If I remove this encoding format, will I break the dependence graph?”
Generally utilized within other tooling, but can be utilized directly by the user
ASPSolverPass
Utilized when an existing analysis pass does not find a specific corner case
Can be used to “programmatically” define new dependence solvers using a specific syntax
Can be utilized as design constraints and/or regression tests to ensure specific functionality/connectivity exists in a design

## Slide 14: CoreGen Infrastructure
All hardware modules/units are defined as DAG nodes
Dependence graph between nodes is “lowered” in multiple stages in order to expose increasing levels of complexity
  Similar to Open64 notion of multi-dimensional IR
DAG Levels:
  Level 0: Basic node connectivity
  Level 1: Expands “extension” nodes to contain all their children
  Level 2: Expands all communication links
  Level 3: Expands all instruction and register encodings
Cache Level
Comm Channel
Core
Instruction
PseudoInst
Encoding
ISA
Register Class
Register
SoC
Spads
VtoP
Plugins

## Slide 15: What type of nodes in the CoreGen IR?
SoC Nodes: Defines a top-level system on chip (one per design)
Core Nodes: Defines a single core with associated ISA and dependent nodes
ISA Nodes: Defines an instruction set architecture container
Instruction Format Nodes: Defines an instruction format with all of its sub-fields
  Sub-fields have properties that define encoding fields, register fields, immediate value fields, etc
Instruction Nodes: Defines a single instruction based upon a prescribed instruction format.
  Ability to define encodings, register classes for register fields, immediate values, etc

## Slide 16: What type of nodes in the CoreGen IR (cont)?
Pseudo Instruction Nodes: Defines specific encodings for existing instructions
  Ability to define prescribed encoding fields as static (eg, immediate = 0x00)
  DOES NOT induce instruction encoding collisions
  EG: ”MOV RT, Ra” = “ADD RT, Ra, $0”
Register Class Nodes: Defines a container node with multiple dependent registers. Register indices within a register class cannot overlap
Register Nodes: Defines a single register node with an index, bit width, sub-register fields and attributes (RO, RW, etc)
Encoding Nodes: Define encodings for parent nodes (EG, register encodings)
Cache Nodes: Defines a single cache layer
  Can be interconnected into multi-level caches

## Slide 17: What type of nodes in the CoreGen IR (cont)?
Communication Channel Nodes: Interconnect multiple nodes via on-chip data+control paths
  Multiple topologies supported
Scratchpad Nodes: Represent addressable on-chip scratchpads
Memory Controller Nodes: Represents a basic memory controller with multiple input/output ports
Virtual to Physical Nodes: Handles virtual to physical memory translation
**Extension Nodes: Special node type that permits users to “import” other CoreGen-developed project artifacts into other projects
  Accelerators are excellent examples of extensions
**Plugin Nodes: Special node type that represents a third-party templated design
  Can contain unlimited number of special properties (not defined by standard CoreGen IR spec)
  May also contain custom code generation facilities to output any style of HDL/RTL, etc

## Slide 18: CoreGen Plugins
CoreGen plugins are containers for self-contained extensions
  Each plugin is effectively its own template
  Bundled as a shared library (can be licensed and distributed outside of System Architect)
These can be:
  Cores, ISAs, cache modules, periphery components, etc
Each plugin can drive unique “code generators” to modify their internal HDL state and/or generate the source compiler
Projects can import any number of plugins
DAG analysis works across plugins
Extension
Plugin
Node
Node
Node
Node
Extension
Plugin
Node
Node
System Architect Project

## Slide 19: CoreGen IR Specification
IR Spec is governed in the same manner as source code development
  Changes to the spec must be received in the form of pull requests on Github
  Adjacent pull requests (that include all the necessary tests) must also exist in CoreGen library tree
  NO changes to the spec are accepted without support in CoreGen
Entire IR spec is documented with examples
Latest revision:
  http://www.systemarchitect.tech/index.php/coregenirspec/

## Slide 20: What is StoneCutter?
StoneCutter is a high level language designed to describe the implementation of a single instruction
  Traditional “C-to-gates” languages/tools were suboptimal given the very large design space
  Each instruction is written as a single “function”
StoneCutter’s syntax is loosely based upon “C”. Support for:
  All rudimentary data types
  Arbitrary bit width data types
  All standard arithmetic operations (+,-,*,/,%,^,|,<<,>>)
  All standard logical operators
  Loops (for, while, do-while)
  Flow control (if/else)
StoneCutter can be written inline within the CoreGen YAML IR
The compiled output is Chisel HDL!

## Slide 21: StoneCutter Tooling
StoneCutter is compiled, not interpreted or simply translated
StoneCutter compiler is based upon LLVM
  Makes heavy use of many traditional LLVM safety and optimization passes
Traditional LLVM compiler passes are augmented with a number of StoneCutter-specific passes
https://llvm.org/Logo.html

## Slide 22: StoneCutter Passes
FieldIO
  Ensures that read-only fields from an instruction payload are not erroneously written to
InstArg
  Ensures instructions are properly using registers as instruction inputs and outputs
InstFormat
  Ensures instruction fields are properly used as arguments to operations
IOWarn
  Warns the user if the instruction utilizes a register that is outside the normal data path for the respective instruction format
SigMap
  Performs global ISA optimization and derives the entire set of signals required as well as the per-instruction signals
PipeBuilder
  Constructs inline pipelines of operations

## Slide 23: Sample StoneCutter Source
instformat Arith.if(reg[GPR] ra,reg[GPR] rb,reg[GPR] rt,enc opc,
enc func,imm imm)
# Register Class Definitions
regclass GPR( u64 r0, u64 r1, u64 r2, u64 r3, u64 r4, u64 r5, u64 r6, u64 r7, u64 r8, u64 r9, u64 r10, u64 r11,
u64 r12, u64 r13, u64 r14, u64 r15, u64 r16, u64 r17, u64 r18, u64 r19, u64 r20, u64 r21, u64 r22, u64 r23,
u64 r24, u64 r25, u64 r26, u64 r27, u64 r28, u64 r29, u64 r30, u64 r31 )
# Instruction Definitions
def add:Arith.if( ra rb rt imm )
{
rt = ra + rb
}
def sub:Arith.if( ra rb rt imm )
{
rt = ra - rb
}

## Slide 24: StoneCutter Language Specification
Language spec is governed in the same manner as source code development
  Changes to the spec must be received in the form of pull requests on Github
  Adjacent pull requests (that include all the necessary tests) must also exist in StoneCutter (CoreGen) library tree
  NO changes to the spec are accepted without support in compiler
Entire language spec is documented with examples
Latest revision:
  http://www.systemarchitect.tech/index.php/stonecutter-language-spec/

## Slide 25: What now?
Level 1 Tutorial: Describes basic design concepts and walks through the initial definition of a RISC-like design
Level 2 Tutorial: Implementing individual instructions using the StoneCutter language and compiler
  Extends the design from Level 1
Level 3 Tutorial: Advanced design and implementation concepts
  Extends the work done in Level 2
Level 4 Tutorial: Building external plugins and integrating external RTL
  How do we integrate existing IP?

## Slide 26: What do you need to continue?
Linux/OSX system with the tools installed
  Prebuilt packages are available:
  https://github.com/opensocsysarch/SystemArchitectRelease
Text editor
  VIM, Emacs, Notepad, etc
For those seeking to use the GUI
  Graphics environment (X11, OSX, etc)
Basic knowledge of computer architecture
Basic knowledge of software architecture

## Slide 27: References
Where do I find more info?

## Slide 28: Web Links
System Architect Public Web
  http://www.systemarchitect.tech/
Documentation
  Latest IR Specification:
    http://www.systemarchitect.tech/index.php/coregenirspec/
Tutorials
  http://www.systemarchitect.tech/index.php/tutorials/
  https://github.com/opensocsysarch/CoreGenTutorials

## Slide 29: Source Code
Main source code hosted on Github:
  https://github.com/opensocsysarch
CoreGen Infrastructure
  https://github.com/opensocsysarch/CoreGen
CoreGenPortal GUI
  https://github.com/opensocsysarch/CoreGenPortal
CoreGen IR Spec
  https://github.com/opensocsysarch/CoreGenIRSpec
System Architect Weekly Development Releases
  https://github.com/opensocsysarch/SystemArchitectRelease

## Slide 30: Contact
Issues should be submitted through the respective Github issues pages (see source code links)
Mailing Lists:
  http://www.systemarchitect.tech/index.php/lists/
Direct developer contacts
  John Leidel: jleidel<at>tactcomplabs<dot>com
  David Donofrio: ddonofrio<at>tactcomplabs<dot>com
  Ryan Kabrick: rkabrick<at>tactcomplabs<dot>com