## Slide 1: Design Concepts with System Architect: Power & Hazard Modeling
John Leidel
Chief Scientist, Tactical Computing Laboratories
ver 2022.09.13

## Slide 2: Tutorial Series
Level 0: Introduction to System Architect
Level 1: System Architect Design Concepts and Developing a basic RISC processor
Level 2: Instruction-Level (StoneCutter) Implementation Concepts
Level 3: Advanced Design Concepts
Level 4: System Architect Plugins and Integrating External RTL
Power and Hazard Modeling with DHDT & POAR

## Slide 3: Overview
Power/Hazard Modeling Tools Overview
POAR Power/Area Modeling
DHDT Power/Hazard Modeling

## Slide 4: Power/Hazard Modeling Tools Overview
System Architect Rapid Design Evaluation Tooling

## Slide 5: System Architect Power/Hazard Modeling Tools
POAR
Coarse grained power and area modeling tool
Utilizes the CoreGen YAML design inputs as the basis for the power/area modeling
Permits user-defined power/area values
  External configuration files that outline power/area for specific hardware units
Permits a user-defined constant routing overhead
  Process-specific routing overhead
Variety of output formats for further processing/analysis
DHDT
Fine grained power and hazard modeling tool
Utilizes the CoreGen YAML and the StoneCutter LLVM IR as the basis for the power/hazard modeling
Constructs a graph of all the candidate signals & clocked pipeline stages for each instruction definition/VLIW stage
Permits user-defined power value inputs
Accepts assembly, binary and hex inputs to track power/hazards for individual instructions with accumulated totals
CSV, ASCI output as well as DOT graph outputs for the internal graph structures

## Slide 6: What do I use and when?
“I want to see basic power/area models”
“I want to compare basic power models across designs”
“I want to see basic design area utilization”
“I want to see per instruction power”
“I want to see detailed power models across different process nodes”
”I want to model VLIW instruction hazards”
POAR
DHDT

## Slide 7: Caveats?
POAR and DHDT are both approximations
  They do not consider switching/transient power
  They have a finite notion of routing congestion (tool dependent)
  They rely upon basic power/area model inputs that are process specific
  YOUR model inputs are YOUR responsibility
We seek to maintain tool performance without sacrificing functionality
If you would like new features, submit a Github Issue!

## Slide 8: POAR Power/Area Modeling
Coarse Grained Power/Area Modeling

## Slide 9: POAR [Power Area Model]
Utilizes the CoreGen design graph input (YAML) to build a graph of included hardware modules
  Optionally also uses the signal maps generated by the StoneCutter tool
For all known design nodes, accumulates total power and total area
  Approximate model of power: TDP
  Approximate model of area: “gates”
Outputs power and area per node type as well as accumulated totals

## Slide 10: POAR Info Options
--help : Prints the help menu
--version : Prints the version info
$> poar --help
$> poar --version

## Slide 11: POAR Runtime Options
Required:
  --design /path/to/CoreGen.yaml : design input
Optional:
  --config /path/to/config.yaml : Sets the power/area node configuration
  -- sigmap /path/to/sigmap.yaml : Stonecutter-generated signal map
  --overhead NN : Sets the constant routing/wire overhead for area calculations
$> poar --design test.yaml
$> poar --design test.yaml --sigmap test_sigmap.yaml
$> poar --design test.yaml --overhead 8.1

## Slide 12: POAR Output Options
Default output is ASCII text printed to the console
Additional output options:
  --text : ASCII text output
  --yaml : YAML output
  --latex : LaTeX output
  -- xml : XML output
$> poar --design test.yaml --text
$> poar --design test.yaml --yaml
$> poar --design test.yaml --latex
$> poar --design test.yaml --xml

## Slide 13: POAR Configuration Options
POWER_REGIBIT: Power per bit in a register
POWER_DPATHBIT: Power per data path bit
POWER_CPATHBIT: Power per control path bit
POWER_CACHEBIT: Power per bit in the cache
POWER_SPADBIT: Power per bit in the scratchpad
POWER_ROMBIT: Power per bit in the internal boot/uCode ROM
POWER_ALUREGBIT: Power per bit in an ALU register
POWER_ALU: Power per ALU bit
POWER_ALUDPATH: Power per ALU data path
POWER_ALUCPATH: Power per ALU control path

## Slide 14: POAR Configuration Options cont.
AREA_REGIBIT: Area per bit in a register
AREA_DPATHBIT: Area per data path bit
AREA_CPATHBIT: Area per control path bit
AREA_CACHEBIT: Area per bit in the cache
AREA_SPADBIT: Area per bit in the scratchpad
AREA_ROMBIT: Area per bit in the internal boot/uCode ROM
AREA_ALUREGBIT: Area per bit in an ALU register
AREA_ALU: Area per ALU bit
AREA_ALUDPATH: Area per ALU data path
AREA_ALUCPATH: Area per ALU control path

## Slide 15: DHDT Power/Hazard Modeling
Fine Grained Power/Hazard Modeling

## Slide 16: DHDT [Deep Hardware Design Tool]
Fine grain power and hazard modeling tool
  Fine grain in the scope of System Architect. NOT equivalent to a SPICE model
Utilizes the CoreGen YAML design input and the StoneCutter compiler IR to build an internal graph representation of the target device
Models individual instructions as they execute (traverse the graph) and accumulate per-instruction power & hazarding
Allows users to investigate how individual instructions behave with respect to power utilization (or groups of instructions)
  Requires the user to input instruction sequences
Outputs data in ASCII and CSV

## Slide 17: DHDT [Deep Hardware Design Tool]

## Slide 18: DHDT [Deep Hardware Design Tool]
DHDT accepts “templates” that describe power values for various hardware subcomponents
  Much like POAR, the power values are relative to a process node
  DHDT power configuration templates contain much more detailed information
Instruction trace inputs are in three forms (one instruction payload per line):
  Assembly: Assembly mnemonics as defined by the CoreGen YAML
  Binary: Binary encoded instruction values prefixed with 0b…
  Hex: Hex encoded instruction values prefixed with 0x…

## Slide 19: DHDT Instruction Trace Inputs
ASM
Binary
Hex

## Slide 20: DHDT Info Options
--help : Prints the help menu
$> dhdt --help

## Slide 21: DHDT Execution Options
--coregen /path/to/coregen.yaml: Utilize the target CoreGen IR
--llvm /path/to/stonecutter.ir: Utilize the target StoneCutter LLVM IR
--inst /path/to/trace.inst: Instruction trace input
Execution types:
  --hazard : Analyze hazards between instructions
  --power : Analyze the power across individual instructions
$> dhdt --coregen ./BasicRISC.yaml --llvm ./BasicRISC.sc.ir --inst test.inst --hazard
$> dhdt --coregen ./BasicRISC.yaml --llvm ./BasicRISC.sc.ir --inst test.inst --power

## Slide 22: DHDT Graph Options
--dot /path/to/graph.dot : Outputs the internal graph structure to a GraphViz DOT file
  This is very handy to investigate idiosyncrasies in the power/hazard output
--output /path/to/output.csv: Outputs the final data to a CSV file
$> dhdt --dot test.dot --coregen ./BasicRISC.yaml --llvm ./BasicRISC.sc.ir --power --inst trace.inst
$> dot -Tpdf test.dot > test.pdf
$> dhdt --coregen ./BasicRISC.yaml --llvm ./BasicRISC.sc.ir --power --inst trace.inst --output out.csv

## Slide 23: DHDT Internal ISA Graph

## Slide 24: Going from YAML to Power/Hazard Output
Step 1: Use CGCLI to generate a singular StoneCutter source file
Step 2: Compile the StoneCutter file to (optimized) LLVM IR
Step 3: Use DHDT to analyze the power/hazard logic
$> cgcli --root ./BasicRISC --ir ./BasicRISC/BasicRISC.yaml --stonecutter
$> sccomp -D --keep -O3 ./BasicRISC/RTL/stonecutter/stonecutter.sc
$> dhdt --coregen ./BasicRISC/BasicRISC.yaml --llvm ./BasicRISC/RTL/stonecutter/stonecutter.sc.ll --inst trace.inst --power
We highly suggest using a Makefile to automate this process!

## Slide 25: What can you do with DHDT?
Example 1: Evaluate a design based upon known power values (using a power template)
Example 2: Evaluate a design against two different power templates that represent different fabs/reticles
Example 3: Evaluate the power of different instruction traces
Example 4: Evaluate two different hardware implementations of the same ISA against the same power template (design trade-off)
Example 5: Evaluate the hazards between multiple instructions

## Slide 26: Things to remember…
The DHDT tool has a simple crack/decode interface
  When using assembly, DHDT assumes that the CoreGen YAML file has `Syntax` entries for each instruction
  The Hex and Binary decode interfaces do not require Syntax interfaces (useful for VLIW stages)
The “simulation” of each instruction payload is rudimentary
  We traverse the subgraph for each instruction payload and accumulate the power for each instruction
  We do not, however, compute bit-level changes of state while we traverse the graph
  The simulation is NOT bit-level accurate (only an approximation)

## Slide 27: References
Where do I find more info?

## Slide 28: Web Links
System Architect Public Web
  http://www.systemarchitect.tech/
Documentation
  Latest StoneCutter Specification:
    http://www.systemarchitect.tech/index.php/stonecutter-language-spec/
Tutorials
  http://www.systemarchitect.tech/index.php/tutorials/
  https://github.com/opensocsysarch/CoreGenTutorials

## Slide 29: Source Code
Main source code hosted on Github:
  https://github.com/opensocsysarch
CoreGen Infrastructure
  https://github.com/opensocsysarch/CoreGen
CoreGenPortal GUI
  https://github.com/opensocsysarch/CoreGenPortal
CoreGen IR Spec
  https://github.com/opensocsysarch/CoreGenIRSpec
StoneCutter Language Spec
  https://github.com/opensysarch/StoneCutterLanguageSpec
System Architect Weekly Development Releases
  https://github.com/opensocsysarch/SystemArchitectRelease

## Slide 30: Contact
Issues should be submitted through the respective Github issues pages (see source code links)
Mailing Lists:
  http://www.systemarchitect.tech/index.php/lists/
Direct developer contacts
  John Leidel: jleidel<at>tactcomplabs<dot>com
  David Donofrio: ddonofrio<at>tactcomplabs<dot>com
  Ryan Kabrick: rkabrick<at>tactcomplabs<dot>com