## Slide 1: Design Concepts with System Architect: Level 1
John Leidel
Chief Scientist, Tactical Computing Laboratories
ver 2018.12.07

## Slide 2: Tutorial Series
Level 1: System Architect Design Concepts and Developing a basic RISC processor
Level 2: Instruction-Level (StoneCutter) Implementation Concepts
Level 3: Advanced Design Concepts
Level 4: System Architect Plugins and Integrating External RTL

## Slide 3: Overview
System Architect Overview
System Architect Tool Infrastructure
Designing a Basic RISC Device
References

## Slide 4: System Architect Overview
Modular, High-Level Design Concepts

## Slide 5: What is System Architect?
A family of tools, APIs and associated infrastructure to permit users to rapidly develop multi-faceted hardware
Utilizes a combination of modular hardware design reuse principles, object oriented development and dependence analysis techniques (compiler theory) to provide an infrastructure for:
  Design & Design Experimentation
  High Level Verification
The artifacts generated by a System Architect design flow include:
  Chisel HDL and Verilog RTL
  C++ cycle-based simulator
  LLVM compiler

## Slide 6: What is System Architect NOT?
System Architect is not the latest C-to-gates tool
  It permits rapid design, verification and reuse
  It does not auto-generate hardware based upon application code
System Architect still relies upon the user to utilize reasonable design concepts
  System Architect will not auto-generate optimized designs based upon unreasonable inputs
  Users need to have a concept of the physical platform (FPGA, ASIC, etc)
System Architect does not currently have a notion of physical layout
  The generated output will not include LUT counts, physical design dimensions or power estimates
  External FPGA/ASIC tools are required for this level of detail

## Slide 7: System Architect Design Flow
Design Input
IR
Verification
Code Generation
Chisel HDL
LLVM Compiler
Verilog
C++ Simulator
User
The user inputs their design using the GUI or text editor. This includes the design parameters and logic for each instruction
The design input is stored in the CoreGen intermediate representation (IR)
The user then executes verification passes against the design in order to ensure the design is correct and optimal. Users have the option of executing special passes to generate design documentation
The user executes the codegen in order to generate the Chisel HDL and/or the LLVM compiler for the target design
The user an now optionally utilize the Chisel HDL to generate the Verilog representation and the C++ simulator. The LLVM compiler can be utilized to drive binary payloads for the C++ simulator
Verilog output can be utilized for downstream synthesis and layout tools

## Slide 8: Typical System Architect Design Flows
Rapid ISA Development
Rapid development of ISA’s with backend RTL and LLVM compiler as artifacts
Cycle-based simulator that supports immediate experimentation
Rapid design evaluation and prototyping
High level verification of design before synthesis
Modular Design
Multi-module design and integration
Integration with other System Architect designs (sub-designs)
External module integration
Plugin support for custom-modularity
Compiler Environment
Auto-generated LLVM compiler infrastructure from design parameters
Modern C/C++ frontend support
  Other frontends can be supported as well
Re-useable as LLVM mainline continues to develop
  Re-spinning entire compiler based on new LLVM versions is automated

## Slide 9: System Architect Infrastructure
CGCLI
Command Line Interface
User Interfaces
CoreGen Infrastructure
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
StoneCutter Compiler
SC Input
SC Input
SC Input
SC Input
SC Input
SC Input
CodeGen
LLVM Source Compiler
Chisel HDL
Backend Infrastructure
YAML
IR
Verilog
C++ Cycle Sim

## Slide 10: How does it work?
We input designs in the user-facing tools and generate CoreGen Intermediate Representation (IR)
The IR preserves the natural dependencies within the design
  Register classes depend upon registers
  Instruction formats depend upon register classes
  Instruction sets depend upon instructions
  Cores require instruction sets
We execute high level verification “passes” against the IR
  Similar in design to traditional compiler passes
  Walks the IR dependence graph and derives properties of the design
  Reports issues in the design infrastructure, outputs interesting data or optimizes the design infrastructure
Users implement instructions in StoneCutter instruction implementation language
  C-like integrated with CoreGen IR to define a single instruction
  Optimized by a traditional compiler flow to generate Chisel HDL for a single instruction
Following the high level verification phase, we execute generate downstream code (code generation)
  Generates Chisel HDL
    Compiled down to Verilog & C++ cycle-based simulator
  Generates LLVM compiler for the target design
Example dependence graph from CoreGen design input

## Slide 11: CoreGen IR Passes
Passes can be selectively enabled or disabled by the user (just like a normal compiler)
Four types of passes
  Analysis
    Analyze the connectivity and the structure of the graph
    Reports back the identified state to the user
    DOES NOT modify the graph (IR is unchanged)
  Optimization
    Optimizes connectivity and structure of the graph
    Much like Kennedy/Callahan dependence analysis/optimization
    MODIFIES the dependence graph (IR is changed)
  Data
    Generates statistical data/output based upon the structure/content of the graph
    EG, outputs a LaTeX specification document based upon the respective ISA
    DOES NOT modify the graph (IR is unchanged)
  System
    Mixtures of each of the aforementioned pass types
    Must be manually instantiated by the tools/users
The internal representation of the IR is stored as a directed acyclic graph (DAG)
Contains four levels that describe varying levels of detail
  This is a performance optimization
  Each subsequent level is a superset of the previous level

## Slide 12: CoreGen IR Passes: Example Analysis Passes
RegSafetyPass/RegIdxPass
Find inconsistencies between registers within the same register file
Multiple registers with the same index
Registers with missing indicies
Registers with prescribed values > than their bit width
Sub-register fields with overlapping names
Sub-register fields with overlapping bit field definitions
EncodingCollisionPass
Identifies potential ISA encoding issues
Utilizes all instruction formats within an ISA
Builds a table of every known instruction within the ISA
  Initializes a bit vector for every instruction using the encoding (eg, opcode), immediate values and register fields (bitmask)
Examines collisions in the “loaded” encodings

## Slide 13: CoreGen IR Passes: Example Data Passes
StatsPass
Walks the entire dependence graph and collects data about the connectivity of the graph and incidence of the nodes
Reports the number of adjacent dependent nodes for each node in the graph (outdegree)
Reports final counts of the incidence of each node type
SpecDoc
Walks the entire dependence graph and collects data about the encoding infrastructure of the ISA and portions of the micro architecture
Outputs a specification document in LaTeX that details each of:
  Register Classes
  Register Encodings
    Subregister encodings (bit fields within register)
  Instruction Formats
  Instruction Encodings
  Master instruction table

## Slide 14: CoreGen IR Passes: Example System Passes
SafeDeletePass
Determines whether removing a node from the graph is safe
For example:
  ”If I remove this register, will I break the dependence graph?”
  “If I remove this encoding format, will I break the dependence graph?”
Generally utilized within other tooling, but can be utilized directly by the user
ASPSolverPass
Utilized when an existing analysis pass does not find a specific corner case
Can be used to “programmatically” define new dependence solvers using a specific syntax
Can be utilized as design constraints and/or regression tests to ensure specific functionality/connectivity exists in a design

## Slide 15: CoreGen Infrastructure
All hardware modules/units are defined as DAG nodes
Dependence graph between nodes is “lowered” in multiple stages in order to expose increasing levels of complexity
  Similar to Open64 notion of multi-dimensional IR
DAG Levels:
  Level 0: Basic node connectivity
  Level 1: Expands “extension” nodes to contain all their children
  Level 2: Expands all communication links
  Level 3: Expands all instruction and register encodings
Cache Level
Comm Channel
Core
Instruction
PseudoInst
Encoding
ISA
Register Class
Register
SoC
Spads
VtoP
Plugins

## Slide 16: What type of nodes in the CoreGen IR?
SoC Nodes: Defines a top-level system on chip (one per design)
Core Nodes: Defines a single core with associated ISA and dependent nodes
ISA Nodes: Defines an instruction set architecture container
Instruction Format Nodes: Defines an instruction format with all of its sub-fields
  Sub-fields have properties that define encoding fields, register fields, immediate value fields, etc
Instruction Nodes: Defines a single instruction based upon a prescribed instruction format.
  Ability to define encodings, register classes for register fields, immediate values, etc

## Slide 17: What type of nodes in the CoreGen IR (cont)?
Pseudo Instruction Nodes: Defines specific encodings for existing instructions
  Ability to define prescribed encoding fields as static (eg, immediate = 0x00)
  DOES NOT induce instruction encoding collisions
  EG: ”MOV RT, Ra” = “ADD RT, Ra, $0”
Register Class Nodes: Defines a container node with multiple dependent registers. Register indices within a register class cannot overlap
Register Nodes: Defines a single register node with an index, bit width, sub-register fields and attributes (RO, RW, etc)
Encoding Nodes: Define encodings for parent nodes (EG, register encodings)
Cache Nodes: Defines a single cache layer
  Can be interconnected into multi-level caches

## Slide 18: What type of nodes in the CoreGen IR (cont)?
Communication Channel Nodes: Interconnect multiple nodes via on-chip data+control paths
  Multiple topologies supported
Scratchpad Nodes: Represent addressable on-chip scratchpads
Memory Controller Nodes: Represents a basic memory controller with multiple input/output ports
Virtual to Physical Nodes: Handles virtual to physical memory translation
**Extension Nodes: Special node type that permits users to “import” other CoreGen-developed project artifacts into other projects
  Accelerators are excellent examples of extensions
**Plugin Nodes: Special node type that represents a third-party templated design
  Can contain unlimited number of special properties (not defined by standard CoreGen IR spec)
  May also contain custom code generation facilities to output any style of HDL/RTL, etc

## Slide 19: CoreGen Plugins
CoreGen plugins are containers for self-contained extensions
  Each plugin is effectively its own template
  Bundled as a shared library (can be licensed and distributed outside of System Architect)
These can be:
  Cores, ISAs, cache modules, periphery components, etc
Each plugin can drive unique “code generators” to modify their internal HDL state and/or generate the source compiler
Projects can import any number of plugins
DAG analysis works across plugins
Extension
Plugin
Node
Node
Node
Node
Extension
Plugin
Node
Node
System Architect Project

## Slide 20: CoreGen IR Specification
IR Spec is governed in the same manner as source code development
  Changes to the spec must be received in the form of pull requests on Github
  Adjacent pull requests (that include all the necessary tests) must also exist in CoreGen library tree
  NO changes to the spec are accepted without support in CoreGen
Entire IR spec is documented with examples
Latest revision:
  http://www.systemarchitect.tech/index.php/coregenirspec/

## Slide 21: System Architect Tool Infrastructure
Tools/API Interfaces for System Architect

## Slide 22: System Architect Tool/API Infrastructure
Infrastructure consists of multiple libraries/APIs
  libCoreGenBackend
  libCoreGenCodegen
  libCoreGenPluginImpl
  libSCComp
  libyamp-cpp
Entire API interface is documented via Doxygen:
  https://codedocs.xyz/opensocsysarch/CoreGen/
User-facing tools include a command line interface and GUI
  Command Line: CGCLI
  GUI: CoreGenPortal
CoreGen
Libraries
libCoreGenPluginImpl
<Plugin>
libCoreGenBackend
libSCComp
libCoreGenCodegen
libyamp-cpp
LLVM Libs
Third-party libraries
CoreGenPortal
CGCLI

## Slide 23: System Architect/CoreGen Libraries
libCoreGenBackend
C++ library that serves as the primary library interface to CoreGen
Handles are CoreGen IR reading/writing
Handles the pass infrastructure
Utilizes libyaml-cpp for reading/writing IR in Yaml form
libCoreGenCodegen
Handles code generation for IR to Chisel translation
Handles code generation for IR to LLVM compiler backend
libSCComp
Implements the StoneCutter language spec
Parser/Lexer/IR all utilize LLVM library interfaces
Code optimization performed via LLVM optimizer
Requires LLVM libraries
**we also have a command interface for the StoneCutter compiler

## Slide 24: Graphical Interface: CoreGenPortal
CoreGenPortal is the primary graphical interface within System Architect
Written in C++
Graphics are handled via wxWidgets
  Currently cross platform support for Linux (Ubuntu, CentOS) and Mac OSX
Use cases
  For those seeking a development environment that resembles traditional IDE’s
  For those unfamiliar/uncomfortable with command line tools

## Slide 25: Command Line Interface: cgcli
Simple, concise command line interface to drive
  Drives all verification passes
  Drives all code generation facilities
Use cases:
  For those who prefer to utilize the command line and write/modify IR using text editors
  To run quick tests against IR
  Regression/CI environments to maintain designs

## Slide 26: CGCLI Info Options
--help : Prints the help menu
--version : Prints the version info
--coregenversion : Prints the CoreGen library version
$> cgcli --help
$> cgcli --version
$> cgcli --coregenversion

## Slide 27: CGCLI Execution Options
Execution options require IR input
  --ir /path/to/IR.yaml
Four execution options:
  --verify : verifies that the CoreGen IR (Yaml) is syntactically correct. Returns a nonzero exit code from CGCLI upon failure
  --pass : executes one or more verification, data or optimization passes
  --chisel: executes the Chisel code generator to output Chisel HDL
  --compiler: executes the LLVM code generator to output LLVM compiler for target design
Options can be combined!
$> cgcli --ir TEST.yaml --verify
$> cgcli --ir TEST.yaml --pass
$> cgcli --ir TEST.yaml --chisel
$> cgcli --ir TEST.yaml --compiler
$> cgcli --ir TEST.yaml --pass --chisel --compiler

## Slide 28: CGCLI Execution Options cont.
Additional options can be utilized
--out /path/to/output.yaml : specifies output yaml file (in the event that you want to preserve existing yaml file)
--dot /path/to/File.dot : generates a Dot (Graphviz) output that represents the dependence graph of the IR in graphical form (see Slide 10)
--project NAME : overrides the project name for the target IR
--root /path/to/project/root/ : overrides the default project root (current working dir)
--archive /path/to/archive/ : overrides the default archive path that contains plugins, LLVM compiler templates, etc
$> cgcli --ir TEST.yaml --dot TEST.dot
$> dot -Tpng TEST.dot > TEST.png

## Slide 29: CGCLI Pass Options
Users can list all the supported passes on the command line
--list-passes: prints a table of all passes, their types and descriptions of what they do
--list-sys-passes: prints a similar table of all the special-purpose system passes
$> cgcli --list-passes
$> cgcli --list-sys-passes

## Slide 30: CGCLI Pass Options cont.
Executing passes is done using the ‘--pass’ option
  By default, all passes noted in ‘--list-passes’ are executed with the --pass option
Each pass runs sequentially and prints any potential faulty state as well as the time required to run each pass
  The larger the graph, the more difficult some passes will be to run
A summary is printed with PASS/FAIL state
  All passes that FAIL will have some notional text describing where the dependence failure occurred in the graph
NOTE: Failed passes don’t necessarily imply the design is broken. Further analysis is required by the user
$> cgcli --ir TEST.yaml --pass

## Slide 31: CGCLI Pass Failures
Any failures will be noted in the pass summary
Look above to the individual pass outputs for the errors reported
Most passes will indicate the exact node name that tripped the failure(s)
$> cgcli --ir TEST.yaml --pass
This indicates that these nodes are not connected and will be optimized out by downstream synthesis tools
Failed Analysis Passes

## Slide 32: CGCLI Pass Options cont.
You can execute the different types of passes with special options
--enable-analysis-passes: Enables only the analysis passes
--enable-data-passes: Enables only the data passes
--enable-opt-passes: Enables only the optimization passes
$> cgcli --ir TEST.yaml --pass --enable-analysis-passes
$> cgcli --ir TEST.yaml --pass --enable-data-passes
$> cgcli --ir TEST.yaml --pass --enable-opt-passes

## Slide 33: CGCLI Pass Options cont.
You can also enable/disable individual passes using their names from the --list-passes option
--enable-pass “PASS1, PASS2”
--disable-pass “PASS1, PASS2”
#-- Only run the DanglingNodePass
$> cgcli --ir TEST.yaml --pass --enable-pass “DanglingNodePass”
#-- Run all passes, but disable the EncodingGapPass
$> cgcli --ir TEST.yaml --pass --disable-pass “EncodingGapPass”

## Slide 34: CGCLI Pass Options cont.
You can execute individual system passes with:
  --enable-sys-pass “PASS1:ARG1,PASS2”
NOTE
  System passes often require arguments in order to execute correctly
  The ”--pass” argument is not required for system passes
#-- Generate the specification doc for the target design
$> cgcli --ir TEST.yaml --enable-sys-pass “SpecDoc:/path/to/output/dir”

## Slide 35: CGCLI Plugin Query
Plugins are external CoreGen modules that are packaged as a shared library object
They utilize a plugin API to drive custom hardware, software and code generation features
These plugins can be licensed and distributed separate from CoreGen
CGCLI provides a command line option to query the special features found in a plugin payload
  --check-plugin “/path/to/plugin”
$> cgcli --check-plugin ”./libSamplePlugin.so"

## Slide 36: Designing a Basic RISC Device
A first conceptual design in System Architect

## Slide 37: Tutorial Source
Tutorial source is published in a Github repository
All design source code is open source under an Apache2 license
  Feel free to reuse it!!
https://github.com/opensocsysarch/CoreGenTutorials
  See the LEVEL1 subdirectory

## Slide 38: Tutorial Assumptions
Standard installation location:
  “/opt/coregen”
  EG, the “cgcli” binary will be located at /opt/coregen/bin/cgcli
  We don’t explicitly reference the fully qualified path in the tutorial
Text editing is required!
  Emacs and Vim are most prevalent, but any standard text editor will suffice
Basic command line knowledge is required
  Executing commands with arguments
Basic knowledge of Git/Github
  Only required if you seek to download/edit the tutorial content

## Slide 39: BasicRISC Core
The remainder of this Level 1 tutorial will focus on constructing a simple RISC core
  Not designed to include every potential bit of functionality
  Simple for a reason!
  Design is open source (Apache license)
We will utilize a text editor to construct the IR by hand
  We will describe the each of the node attributes by hand as we go along
Our basic core will support:
  General purpose registers
  Control registers
  Simple instruction format
  Memory I/O, basic arithmetic, control flow instructions
RISC ALU
General Purpose Registers
Control Registers
Memory Interface

## Slide 40: BasicRISC ISA
Traditional RISC ISA
  Opcodes (opc) determine the “class” of instructions
  Function codes (func) determine the target instruction
  Instructions are grouped by their argument types:
    INST GPR, GPR, GPR
    INST GPR, CTRL, GPR
    INST CTRL, GPR, GPR
  Plenty of opcode/function space to expand for your own use
Arithmetic:
  Integer arithmetic (2’s-complement)
  Add, Sub, Mul, Div
  Logical/Arithmetic shifts
  Logicals (AND, OR, NAND, NOR, XOR, NOT)
Comparisons:
  Compare {NE, EQ, GT, LT, GTE, LTE}
Branches
  Conditional and unconditional
  Absolute and relative (jump)
See BasicRISCInstTable for a full instruction set listing

## Slide 41: Directly Editing CoreGen Yaml IR
Yaml IR is ASCII text
Hierarchy is determined by indentions
  Indentions are SPACES, not tabs
  Each indentation should be two (2) spaces
You can use any potential editor!
A few important notes:
  Nodes are parsed in the correct order regardless of their order in the file
    We do this to preserve the natural hierarchy and dependence between nodes
  Node names are case sensitive
    “RegName” != “Regname”
  Certain nodes have required and optional attributes
    Refer to the IR documentation for what is optional
  Comments are delineated with ‘#’ characters
    Similar to BASH shell scripts
#-- this is a comment
NODE:
- SubNode: Name1
Attribute1: 64
Attribute2: false
Attribute3: This_Is_A_String
- SubNode: FOO
Bars:
- bar0
- bar1
- bar2
Example CoreGen Yaml IR Formatting

## Slide 42: Ten Design Steps for Level 1
Step 1: Build our project skeleton
Step 2: Begin editing Yaml IR file by defining project infrastructure
Step 3: Define the register infrastructure
Step 4: Define the ISA
Step 5: Define the instruction format
Step 6: Define the instructions
Step 7: Define the pseudo instructions
Step 8: Define a cache
Step 9: Define a core
Step 10: Define an SoC
The CoreGen IR for each step is outlined in ~/CoreGenTutorials/LEVEL1/StepN

## Slide 43: Step 1: Build the Project Skeleton
Create a new directory to hold all your project-related files
  All the generated artifacts will reside within this top-level directory
Create a basic Yaml IR file using your preferred text editor
  BasicRISC.yaml
Add some header information to describe the file
  Remember: comments are denoted using ‘#’
  Multi-line comments need a new ‘#’ for every new line
~/CoreGenTutorials/LEVEL1/Step1
#---------------------------------------------------
#--- BasicRISC.yaml
#
# My first CoreGen Design Experiment
#---------------------------------------------------

## Slide 44: Step 2: Define the project information
Now we need to create a new project
  Describes the name and type of the project
  Helps optimize code generation for different project types
  Future support for different Chisel or LLVM backends
Create a new “ProjectInfo” node block as shown here
~/CoreGenTutorials/LEVEL1/Step2
#---------------------------------------------------
#--- BasicRISC.yaml
#
# My first CoreGen Design Experiment
#---------------------------------------------------
# -------------------------------------------------------
# ProjectInfo Section
# -------------------------------------------------------
ProjectInfo:
- ProjectName: BasicRISC
ProjectRoot: ./
ProjectType: soc
ChiselMajorVersion: 3
ChiselMinorVersion: 0

## Slide 45: Step 2: Define the project information cont.
Parameters:
  ProjectName: Name of the project. Utilized downstream by the generated LLVM compiler to define the architecture target
  ProjectRoot: The source directory of the project. Usually “./”. Can point at other directories
  ProjectType: Defines the ”style” of the project
  ChiselMajorVersion: Defines the major version for the generated Chisel
  ChiselMinorVersion: Defines the minor version for the generated Chisel
Project Types
  soc: System on chip designs with connectivity between heterogeneous modules/cores as well as internal and/or external memories
  module: Hardware entities that are effectively self contained. Will contain a small number of disparate node types
  extension: Hardware entities that include hierarchies of modules. EG, an accelerator with its respective ISA
  unknown: Projects that don’t fit any of the aforementioned models
Chisel Versions
  Currently only supports “3” & “0” for Chisel 3.0
~/CoreGenTutorials/LEVEL1/Step2

## Slide 46: Step 3: Define the register infrastructure
Now we begin adding registers to our design
All the registers are added in a single Registers node block
  We will separate them into register classes in Step 4
Registers must have unique names
  Each register will have a multitude of parameters
~/CoreGenTutorials/LEVEL1/Step3
Registers:
- RegName: r0
Width: 64
Index: 0
PseudoName: zero
IsFixedValue: true
FixedValue: 0
IsSIMD: false
RWReg: false
ROReg: true
CSRReg: false
AMSReg: false
TUSReg: false
Shared: false
Lets start by adding an r0 register as shown here
A few interesting things to note:
  As with other RISC ISAs, r0 is hardwired to “0”
  Read-Only register

## Slide 47: Step 3: Define the register infrastructure cont.
Parameters
  RegName: unique name of the register used in assembly code
  Width: width of the register in bits
    All of our registers here will be 64 bits
  Index: the index within the respective register class, must be unique within the register class
  PseudoName:
    [Optional] Pseudo name that be also be utilized in assembly
~/CoreGenTutorials/LEVEL1/Step3
Registers:
- RegName: r0
Width: 64
Index: 0
PseudoName: zero
IsFixedValue: true
FixedValue: 0
IsSIMD: false
RWReg: false
ROReg: true
CSRReg: false
AMSReg: false
TUSReg: false
Shared: false
Parameters
  IsFixedValue: Is this register hardwired to a fixed value? If ‘true’, then we must also have a “FixedValue” parameter
  FixedValue: the decimal value of the hardwired register

## Slide 48: Step 3: Define the register infrastructure cont.
Parameters
  IsSIMD: Is the register a SIMD register?
  RWReg: Can we read and write this register?
  ROReg: Is this register Read-Only (from assembly)?
  CSRReg: Is this a configuration/status register? Generally considered to be on slow data path
~/CoreGenTutorials/LEVEL1/Step3
Registers:
- RegName: r0
Width: 64
Index: 0
PseudoName: zero
IsFixedValue: true
FixedValue: 0
IsSIMD: false
RWReg: false
ROReg: true
CSRReg: false
AMSReg: false
TUSReg: false
Shared: false
Parameters
  AMSReg: Is this an arithmetic machine state register? This forces the registers to reside within the ALU pipeline
  TUSReg: Is this register shared across thread units? Thread units are duplicated register files for symmetric multi-threading within a core. If set to false, then each thread unit will get a unique copy of this register
  Shared: Is this register shared across multiple cores? Configuration registers are generally shared

## Slide 49: Step 3: Register Parameters
REGISTER
Register
Data Path
ALU/
Pipeline
ALU
RWReg=true
REGISTER
ALU/
Pipeline
ROReg=true
ALU/
Pipeline
IsSIMD=true
REGISTER
ALU/
Pipeline
CSRReg=true
ALU/
Pipeline
AMSReg=true
REGISTER
TUSReg=true
ALU/
Pipeline
TUSReg=true
TUSReg=false
TUSReg=false
ALU/
Pipeline
Shared=true
ALU/
Pipeline
REGISTER

## Slide 50: Step 3: Define the register infrastructure cont
Now add the remainder of the general purpose registers
  Add these within the existed Registers block
The naming convention used here is:
  r1 - r31
~/CoreGenTutorials/LEVEL1/Step3
- RegName: r1
Width: 64
Index: 1
IsFixedValue: false
FixedValue: 0
IsSIMD: false
RWReg: true
ROReg: false
CSRReg: false
AMSReg: false
TUSReg: false
Shared: false
Remember:
  Each needs a unique Index value
  Make the remainder of the registers ReadWrite
  Don’t require PseudoNames or FixedValues
    Feel free to add PseudoName values at your leisure

## Slide 51: Step 3: Define the register infrastructure cont.
Now we need to add our control registers
  Notice that we restart the indexing at 0
  We will compose two separate register files
Read-Only Control Regs:
  PC: program counter
  EXC: exception flags
    More on this in future tutorials
  NE: Not equal
  EQ: Equal
  GT: Greater Than
  LT: Less Than
  GTE: Greater than or equal to
  LTE: Less than or equal to
~/CoreGenTutorials/LEVEL1/Step3
Read-Write Control Regs:
  SP: stack pointer
  FP: frame pointer
  RP: return pointer
Comparison registers (NE, EQ, etc) are utilized for flow control and branches
#-- compare two registers; place result in r7
LABEL:
#-- compare two registers;
#-- place result in r7
cmp.eq r7,r5,r6
#-- if the result was eq, take the branch
brac LABEL, r7, eq

## Slide 52: Step 3: Define the register infrastructure cont.
Comparison registers
  Each comparison register has a fixed value associated with it
  Fixed values map to the corresponding function code for respective compare instruction
    More on this in Step 5 & 6
~/CoreGenTutorials/LEVEL1/Step3
Fixed Values
  NE = 2
  EQ = 3
  GT = 4
  LT = 5
  GTE = 6
  LTE = 7
Why is the PC Read-Only?
  We do not permit instructions to directly modify the PC as a register argument
  Inherently dangerous!

## Slide 53: Step 3: Define the register infrastructure cont.
Now that we have our registers defined, we need to create two register classes:
  GPR: {r0-r31}
  CTRL: {pc, exc, ne, etc}
Create a new node block called RegClasses
~/CoreGenTutorials/LEVEL1/Step3
RegClasses:
- RegisterClassName: GPR
Registers:
- r0
- r1
…..
- r31
- RegisterClassName: CTRL
Registers:
- pc
- exc
- ne
- eq
….
- rp
Parameters
  RegisterClassName: Unique name associated with each register class. Utilized to specify permissible registers in the instruction format register fields.
  Registers: Defines the set of registers in our register class. Using the names from the Registers block, add each of the registers to the register class

## Slide 54: Step 3: Define the register infrastructure cont.
Now that we have all our registers defined, lets utilize System Architect to verify the design so far
Utilize the “cgcli” tool to run all of our passes
FAILED!?
~/CoreGenTutorials/LEVEL1/Step3
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass
Failed Analysis Passes

## Slide 55: Step 3: Define the register infrastructure cont.
Lets analyze why this failed:
DanglingRegionPass
  Finds the number of unique, unconnected regions of nodes
  Graph theory: community detection
  We had two unconnected regions
  Why??
Lets utilize the graphing function to examine the dependence graph
~/CoreGenTutorials/LEVEL1/Step3
$> cgcli --ir ./BasicRISC.yaml --dot Step3.dot
$> dot -Tpng Step3.dot > Step3.png
CTRL Register File
GPR Register File
We have two, unique register files that aren’t yet connected to anything useful. Hence, two unconnected regions of hardware!

## Slide 56: Step 4: Define an instruction set
Now that we have registers and register classes, we need an instruction set container
ISA nodes have a single parameter that identifies a unique ISA name
You can include an unlimited number of unique ISAs in a design
ISA nodes are ”containers”
  We will utilize them in future steps to organize instructions and register classes into an instruction set implementation
Define an ISAs node block
~/CoreGenTutorials/LEVEL1/Step4
ISAs:
- ISAName: BasicRISC.ISA
Parameters
  ISAName: Unique name for an instruction set

## Slide 57: Step 4: Define an instruction set cont.
Now that we have all our instruction set defined, lets rerun our analysis passes
Utilize the “cgcli” tool to run all of our passes
FAILED AGAIN!?
~/CoreGenTutorials/LEVEL1/Step4
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass
Failed Analysis Passes

## Slide 58: Step 4: Define an instruction set cont.
The DanglingRegionPass fails for the same reason as in Step 3
  Multiple unconnected regions
The DanglingNodePass fails because our new ISA isn’t utilized in any cores yet
Lets utilize CGCLI to rerun our passes and ignore these two analysis passes
  Success!
~/CoreGenTutorials/LEVEL1/Step4
$> cgcli --ir ./BasicRISC.yaml --pass --disable-pass "DanglingRegionPass,DanglingNodePass"
Dangling ISA Node

## Slide 59: Step 5: Define the instruction format(s)
Now that we have our ISA ready to receive instructions and our register classes ready to be utilized, we can begin defining instruction formats
Instruction formats can contain an unlimited number of fields in any bit width
  RISC is not required
Three types of fields are supported
  Encoding Fields: Hardwired encodings for individual instructions
  Register Fields: Inserted by the assembler and utilized as indices into hardware state
  Immediate Value Fields: Inserted by the assembler and utilized as literal values by the instruction
~/CoreGenTutorials/LEVEL1/Step5
RA: register input
RB: register input
RT: register output (target)
OPC: opcode encoding
FUNC: function encoding
IMM: immediate value
BasicRISC Includes 6 Fields across 32 bits of encoding

## Slide 60: Step 5: Define the instruction format(s) cont.
For each Register Field, we assign a single register class
  Enables the correct data path for the respective register index into the correct register file
BasicRISC will include three instruction formats to support our three variants of register arguments
~/CoreGenTutorials/LEVEL1/Step5
INST Rt, Ra, Rb | 
Instruction Format Mnemonic | Register Class Arguments
Arith.if | INST GPR, GPR, GPR
ReadCtrl.if | INST GPR, GPR, CTRL
WriteCtrl.if | INST CTRL, GPR, GPR

## Slide 61: Step 5: Define the instruction format(s) cont.
Create a new top-level node InstFormats
Each format must have a unique name, instruction set container and width
Users can define any number of subfields
  Subfields must have at least 1 bit
  Maximum is the bit width of the encoding
Note: You are NOT required to specify all the bits in the encoding
  The EncodingGapPass will tell you if you have unused space
InstFormats:
- InstFormatName: Arith.if
ISA: BasicRISC.ISA
FormatWidth: 32
Fields:
Parameters
  InstFormatName: Contains a unique instruction format name (utilized downstream by instruction definitions)
  ISA: Specifies the instruction set container (Step 4)
  FormatWidth: Defines the total width (in bits) for the encoding format
  Fields: Contains the definitions of all the subfields
~/CoreGenTutorials/LEVEL1/Step5

## Slide 62: Step 5: Define the instruction format(s) cont.
Field Parameters
  StartBit: The starting bit of the respective field
  EndBit: The ending bit of the respective field
  MandatoryField: Determines whether any downstream instruction encodings are REQUIRED to specify a unique value for this field
    EG, opcodes and function codes MUST be specified!
~/CoreGenTutorials/LEVEL1/Step5
Field Parameters
  FieldName: unique name (within the respective format) to describe a field
  FieldType: The type of encoding:
    CGInstReg: Register class fields (must include a RegClass attribute
    CGInstCode: Instruction encoding field
    CGInstImm: Immediate values
  FieldWidth: The total width (in bits) for the encoding
Field Parameters
  RegClass: Defines the register class for the associated CGInstReg field. The names of the register classes much match those defined in RegClasses section from Step 3

## Slide 63: Step 5: Define the instruction format(s) (Arith.if)
InstFormats:
- InstFormatName: Arith.if
ISA: BasicRISC.ISA
FormatWidth: 32
Fields:
- FieldName: ra
FieldType: CGInstReg
FieldWidth: 5
StartBit: 0
EndBit: 4
MandatoryField: false
RegClass: GPR
~/CoreGenTutorials/LEVEL1/Step5
- FieldName: rb
FieldType: CGInstReg
FieldWidth: 5
StartBit: 5
EndBit: 9
MandatoryField: false
RegClass: GPR
- FieldName: rt
FieldType: CGInstReg
FieldWidth: 5
StartBit: 10
EndBit: 14
MandatoryField: false
RegClass: GPR
- FieldName: opc
FieldType: CGInstCode
FieldWidth: 5
StartBit: 15
EndBit: 19
MandatoryField: true
- FieldName: func
FieldType: CGInstCode
FieldWidth: 5
StartBit: 20
EndBit: 24
MandatoryField: true
- FieldName: imm
FieldType: CGInstImm
FieldWidth: 7
StartBit: 25
EndBit: 31
MandatoryField: false

## Slide 64: Step 5: Define the instruction format(s) (ReadCtrl.if)
InstFormats:
- InstFormatName: Read.if
ISA: BasicRISC.ISA
FormatWidth: 32
Fields:
- FieldName: ra
FieldType: CGInstReg
FieldWidth: 5
StartBit: 0
EndBit: 4
MandatoryField: false
RegClass: GPR
~/CoreGenTutorials/LEVEL1/Step5
- FieldName: rb
FieldType: CGInstReg
FieldWidth: 5
StartBit: 5
EndBit: 9
MandatoryField: false
RegClass: CTRL
- FieldName: rt
FieldType: CGInstReg
FieldWidth: 5
StartBit: 10
EndBit: 14
MandatoryField: false
RegClass: GPR
- FieldName: opc
FieldType: CGInstCode
FieldWidth: 5
StartBit: 15
EndBit: 19
MandatoryField: true
- FieldName: func
FieldType: CGInstCode
FieldWidth: 5
StartBit: 20
EndBit: 24
MandatoryField: true
- FieldName: imm
FieldType: CGInstImm
FieldWidth: 7
StartBit: 25
EndBit: 31
MandatoryField: false

## Slide 65: Step 5: Define the instruction format(s) (WriteCtrl.if)
InstFormats:
- InstFormatName: Read.if
ISA: BasicRISC.ISA
FormatWidth: 32
Fields:
- FieldName: ra
FieldType: CGInstReg
FieldWidth: 5
StartBit: 0
EndBit: 4
MandatoryField: false
RegClass: GPR
~/CoreGenTutorials/LEVEL1/Step5
- FieldName: rb
FieldType: CGInstReg
FieldWidth: 5
StartBit: 5
EndBit: 9
MandatoryField: false
RegClass: GPR
- FieldName: rt
FieldType: CGInstReg
FieldWidth: 5
StartBit: 10
EndBit: 14
MandatoryField: false
RegClass: CTRL
- FieldName: opc
FieldType: CGInstCode
FieldWidth: 5
StartBit: 15
EndBit: 19
MandatoryField: true
- FieldName: func
FieldType: CGInstCode
FieldWidth: 5
StartBit: 20
EndBit: 24
MandatoryField: true
- FieldName: imm
FieldType: CGInstImm
FieldWidth: 7
StartBit: 25
EndBit: 31
MandatoryField: false

## Slide 66: Step 5: Define the instruction format(s) cont.
~/CoreGenTutorials/LEVEL1/Step5
Notes on defining instruction fields:
  The tools support an unlimited number of formats
  Use consistent naming conventions for your fields
    You will utilize these downstream when defining each instruction
  Single bit control fields are permitted
    The EncodingGapPass will flag any formats that do not utilize every bit in the total encoding space
    Even if bits are unused, its wise to mark them as fields in the format
  Encoding fields are not bound to nibble/byte boundaries
    The tools support arbitrarily complex encodings in non-byte aligned fields
    Instruction fetches will always be on byte boundaries
    Encoding orthogonal instruction formats in the final ELF binaries is more difficult and will waster space
      EG, 129 bit instructions

## Slide 67: Step 5: Define the instruction format(s) cont.
Now that we have all our instruction set formats defined, lets rerun our analysis passes
Utilize the “cgcli” tool to run all of our passes
Everything passes!
  Our register files are now dependencies within the instruction encodings!
~/CoreGenTutorials/LEVEL1/Step5
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass

## Slide 68: Step 5: Define the instruction format(s) cont.
~/CoreGenTutorials/LEVEL1/Step5

## Slide 69: Step 6: Define the instructions
Now that we have our instruction formats completed, we need to define our instructions
Refer to the BasicRISCInstTable documents in the LEVEL1 tutorial directory for a full listing of the instructions and their associated encoding values
Start by adding a top-level node block for Insts
~/CoreGenTutorials/LEVEL1/Step6
Insts:
- Inst: add
ISA: BasicRISC.ISA
InstFormat: Arith.if
Encodings:
- EncodingField: opc
EncodingWidth: 5
EncodingValue: 0
- EncodingField: func
EncodingWidth: 5
EncodingValue: 0
- EncodingField: imm
EncodingWidth: 7
EncodingValue: 0
Parameters:
  ISA: Defines the instruction set that this instruction resides within (Step 4)
  InstFormat: Defines the instruction format utilized to encode this instruction (Step 5)
  Encodings: Defines the set of encodings uniquely identifying this instruction

## Slide 70: Step 6: Define the instructions cont.
Each of the encodings utilizes a field from our instruction format (Step 5)
The names MUST match
  They are case sensitive
Each field must have a value and a width
The field width must be <= the width of the field in the instruction format
  We check the encoding value against the field width
  This can be utilized for advanced designs in the future
~/CoreGenTutorials/LEVEL1/Step6
Insts:
- Inst: add
ISA: BasicRISC.ISA
InstFormat: Arith.if
Encodings:
- EncodingField: opc
EncodingWidth: 5
EncodingValue: 0
- EncodingField: func
EncodingWidth: 5
EncodingValue: 0
- EncodingField: imm
EncodingWidth: 7
EncodingValue: 0
Encodings:
  EncodingField: The instruction format field this encoding applies to
  EncodingWidth: The width of the encoding (in bits)
  EncodingValue: The decimal value you are encoding

## Slide 71: Step 6: Define the instructions cont.
The tutorial slides do not introduce each instruction
Its up to you to complete the remainder of the instructions using the documented encodings
  Optionally utilize the design files provided for you
There are 41 instructions defined in BasicRISC
~/CoreGenTutorials/LEVEL1/Step6
For instructions that don’t utilize the immediate field, we hardwire its value to zero
  Isn’t necessary, but good practice
Use the tools to check your encodings!
The EncodingCollisionPass will find all potential collisions in the encoded space
  Will report which instructions contain the collisions
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass --enable-pass "EncodingCollisionPass"

## Slide 72: Step 6: Define the instructions cont.
~/CoreGenTutorials/LEVEL1/Step6
$> cgcli --ir ./BasicRISC.yaml --dot Step6.dot
$> dot -Tpng Step3.dot > Step6.png
This is a snapshot of our instruction set definition in the dot graph output with all the encodings expressed
Notice how the encodings for each field are mapped in the dependence graph:
  INSTRUCTION_NAME:FIELD_NAME
  Enables easier visual debugging of dependence/encoding issues

## Slide 73: Step 7: Define the pseudo instructions
Now that we have our instructions defined, we can optionally define some pseudo instructions
Pseudo instructions are instruction aliases to make for clear, concise assembly language
For example
  mov Rt, Ra = add Rt, Ra, 0
The pseudo instructions don’t cost any additional hardware
  They’re only expressed in the compiler/assembler
Our BasicRISC design has three pseudo instructions
  Move GPR -> GPR
  Move CTRL -> GPR
  Move GPR -> CTRL
Refer to the BasicRISCInstTable documents
~/CoreGenTutorials/LEVEL1/Step7
PseudoInsts:
- PseudoInst: mov
ISA: BasicRISC.ISA
Inst: add
Encodings:
- EncodingField: ra
EncodingWidth: 5
EncodingValue: 0
Add a top-level PseudoInst node block
Parameters:
  PseudoInst: The unique name of the pseudo instruction
  ISA: The containing ISA
  Inst: The base instruction that is aliased
  Encodings: Contains a set of special encodings for this pseudo instruction

## Slide 74: Step 7: Define the pseudo instructions cont.
Encodings:
  EncodingField: The instruction format field this encoding applies to
  EncodingWidth: The width of the encoding (in bits)
  EncodingValue: The decimal value you are encoding
~/CoreGenTutorials/LEVEL1/Step7
PseudoInsts:
- PseudoInst: mov
ISA: BasicRISC.ISA
Inst: add
Encodings:
- EncodingField: ra
EncodingWidth: 5
EncodingValue: 0
In this example, we are forcing the Ra field to always be “0”
  This forces Ra = register R0 (which is hardwired to zero
Notes on pseudo instructions
  You can define multiple pseudo instructions that alias a single instruction
  You can override any of the register field and immediate encodings
  You CANNOT override the encoding fields

## Slide 75: Step 7: Define the pseudo instructions cont.
~/CoreGenTutorials/LEVEL1/Step7
PseudoInsts:
- PseudoInst: mov
ISA: BasicRISC.ISA
Inst: add
Encodings:
- EncodingField: ra
EncodingWidth: 5
EncodingValue: 0
Now our pseudo instructions are depicted in the dependence graph
Note how they depend upon the original instruction definitions
Removing the original instructions will break the dependence graph and the tools will warn the user of the issue

## Slide 76: Step 8: Define a cache
Now we begin adding memory units to our design: Caches
Caches are optional components in your designs
  Not required, but advantageous for performance
  Absence of caches will force instruction fetches from memory
Caches can also be hierarchical
  We have a single cache layer in BasicRISC, but it is trivial to add hierarchical caches
Create a Caches node block
~/CoreGenTutorials/LEVEL1/Step8
Caches:
- Cache: Core0.L1.cache
Sets: 2
Ways: 8
Parameters:
  Cache: The unique name of the cache level. These names must be unique across ALL cores within a SoC
  Sets: The number of sets in the cache blocking configuration
  Ways: The number of ways in the cache tagging configuration
  SubLevel: Optional parameter that describes a connected sub-cache
    The L2 would be a sublevel from L1

## Slide 77: Step 8: Define a cache cont.
Notes on cache configuration
  The dependence infrastructure in CoreGen derives local versus shared caches
  Caches are not required to be homogeneous between layers
  Designs can contain an unlimited number of caching layers
~/CoreGenTutorials/LEVEL1/Step8
Caches:
- Cache: Core0.L1.cache
Sets: 2
Ways: 8
SubLevel: Core0.L2.cache
- Cache: Core0.L2.cache
Sets: 4
Ways: 8
SubLevel: Shared.L3.cache
- Cache: Shared.L3.cache
Sets: 2
Ways: 8
Shared.L3.cache
Core0.L2.cache
Core0.L1.cache
Core1.L2.cache
Core1.L1.cache

## Slide 78: Step 8: Define a cache cont.
Executing the cgcli passes against our design in Step 8 will uncover dangling nodes and dangling regions
Our caches are not yet connected to cores!
~/CoreGenTutorials/LEVEL1/Step8
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass
Failed Analysis Passes

## Slide 79: Step 9: Define a core
Now that we have a cache (or cache hierarchy), lets define a core
Cores are containers that include lower-level modules and data/control paths
Cores implement an instruction set with a set of register classes
  The register sharing attributes are defined by the individual registers
Cores can also enable symmetric multi-threading (SMT) by specifying multiple “ThreadUnits”
  The default is ‘1’ if unspecified
Define a Cores node block
~/CoreGenTutorials/LEVEL1/Step9
Cores:
- Core: core0
ThreadUnits: 1
Cache: Core0.L1.cache
ISA: BasicRISC.ISA
RegisterClasses:
- RegClass: GPR
- RegClass: CTRL
Parameters:
  Core: Name of the respective core. Must be unique
  ThreadUnits: The number of symmetric thread units within the core
  Cache: The connected cache hierarchy (usually L1)
    This is technically optional, but definitely useful for at least instruction cache space
  ISA: Links the respective instruction set to be utilized by the core
  RegisterClasses: List of register classes required to implement the ISA

## Slide 80: Step 9: Define a core cont.
Lets verify our work thus far
Utilize the “cgcli” tool to run all of our passes
One failure
  CoreSafetyPass
    Identified our core that is not connected to an SoC!
    This is fine for extension and module projects
    For SoC projects, we need a top-level SoC container
~/CoreGenTutorials/LEVEL1/Step9
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass

## Slide 81: Step 10: Define an SoC
The final step is to define a top-level system-on-chip (SoC) container
  Generally only utilized in “soc” designs
  Generally only one SoC per design
Define a Socs node block
Parameters:
  Soc: Defines the name of the top-level SoC container
  Cores: Defines the cores that are contained within the SoC (from Step 9)
~/CoreGenTutorials/LEVEL1/Step10
Socs:
- Soc: BasicRISC.soc
Cores:
- Core: core0

## Slide 82: Step 10: Define an SoC cont.
Now that everything is defined, lets run the tools and check for issues
Utilize the “cgcli” tool to run all of our passes
Everything passes!
~/CoreGenTutorials/LEVEL1/Step10
$> cgcli --ir ./BasicRISC.yaml --verify
$> cgcli --ir ./BasicRISC.yaml --pass

## Slide 83: Step 10: Define an SoC cont.
~/CoreGenTutorials/LEVEL1/Step10
Our fully encapsulated design with all the encodings expanded in the dependence graph!

## Slide 84: References
Where do I find more info?

## Slide 85: Web Links
System Architect Public Web
  http://www.systemarchitect.tech/
Documentation
  Latest IR Specification:
    http://www.systemarchitect.tech/index.php/coregenirspec/
Tutorials
  http://www.systemarchitect.tech/index.php/tutorials/
  https://github.com/opensocsysarch/CoreGenTutorials

## Slide 86: Source Code
Main source code hosted on Github:
  https://github.com/opensocsysarch
CoreGen Infrastructure
  https://github.com/opensocsysarch/CoreGen
CoreGenPortal GUI
  https://github.com/opensocsysarch/CoreGenPortal
CoreGen IR Spec
  https://github.com/opensocsysarch/CoreGenIRSpec
System Architect Weekly Development Releases
  https://github.com/opensocsysarch/SystemArchitectRelease

## Slide 87: Contact
Issues should be submitted through the respective Github issues pages (see source code links)
Mailing Lists:
  http://www.systemarchitect.tech/index.php/lists/
Direct developer contacts
  John Leidel: jleidel<at>tactcomplabs<dot>com
  Frank Conlon: fconlon<at>tactcomplabs<dot>com