## Slide 1: Design Concepts with System Architect: Level 2
John Leidel
Chief Scientist, Tactical Computing Laboratories
ver 2022.09.13

## Slide 2: Tutorial Series
Level 0: Introduction to System Architect
Level 1: System Architect Design Concepts and Developing a basic RISC processor
Level 2: Instruction-Level (StoneCutter) Implementation Concepts
Level 3: Advanced Design Concepts
Level 4: System Architect Plugins and Integrating External RTL

## Slide 3: Overview
StoneCutter Overview
StoneCutter Tool Infrastructure
Intro to StoneCutter Syntax
Implementing a Basic RISC Device
References

## Slide 4: StoneCutter Overview
Instruction Definition Concepts

## Slide 5: What is StoneCutter?
A concise language for specifying the implementation of a SINGLE instruction
StoneCutter implements instructions as “functions”
Supports all the standard types of:
  Arithmetic
  Boolean logic
  Conditionals/Flow control
Support for pathological, optimized circuits via “intrinsics”
  Similar in style to traditional compiler builtins/intrinsics
Language is constructed to support very rapid design evaluation
StoneCutter tools compile to Chisel HDL

## Slide 6: What is StoneCutter NOT?
StoneCutter is not the latest C-to-gates language
  Does not compile directly to Verilog
StoneCutter is not designed to implement the entire design
  The language constructs are only designed to handle individual instructions
StoneCutter still relies upon the user to utilize reasonable design concepts
  StoneCutter has a number of safety passes in order to error/warn the user of erroneous or potentially slow paths
  Is not guaranteed to produce optimized implementations from poor inputs
StoneCutter does not have a notion of physical layout
  We’re compiling to Chisel HDL, not gates
StoneCutter does not have explicit access to clocks
  Clocks are exposed in the Chisel, but not StoneCutter

## Slide 7: System Architect Infrastructure
CGCLI
Command Line Interface
User Interfaces
CoreGen Infrastructure
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
CoreGen Plugin
StoneCutter Compiler
SC Input
SC Input
SC Input
SC Input
SC Input
SC Input
CodeGen
LLVM Source Compiler
Chisel HDL
Backend Infrastructure
YAML
IR
Verilog
C++ Cycle Sim
This is where StoneCutter fits

## Slide 8: StoneCutter Infrastructure
Users craft StoneCutter implementation files that represent their instructions
  Each instruction implementation is a “function” with inputs and outputs
StoneCutter implementation files are compiled via the StoneCutter compiler (sccomp)
StoneCutter compiler is based upon LLVM
  Custom language frontend & custom code generator
Compiler utilizes mixture of traditional LLVM optimization passes and custom language passes
  We encapsulate circuit-specific logic in our custom passes

## Slide 9: StoneCutter Infrastructure
StoneCutter Instruction Definitions
CoreGen Instruction Formats
CoreGen Register Files
SCCOMP
Command Line Interface
StoneCutter Language Parser
LLVM IR
Traditional LLVM Optimization Passes
StoneCutter Custom Optimization Passes
StoneCutter Safety Optimization Passes
StoneCutter Chisel Code Generator

## Slide 10: Example LLVM Optimization Passes
CFGSimplicationPass
Performs dead code elimination and basic block merging
Removes basic blocks with no predecessors
Merges basic blocks with simple control flows
Eliminates PHI nodes for basic blocks with single predecessors
Eliminates basic blocks with only unconditional branches
https://llvm.org/docs/Passes.html#simplifycfg-simplify-the-cfg
LICMPass
Performs “Loop Invariant Code Motion”
Attempts to remove code from loop bodies
”Hoists” or “Sinks” unnecessary code out of loops in order to minimize redundant operations
Will reduce downstream size of iterative loop circuits
https://llvm.org/docs/Passes.html#licm-loop-invariant-code-motion

## Slide 11: Example StoneCutter Safety Passes
FieldIO
Walks all the statements that write to an output value
Ensures that these output values are permissible output fields
The following values/fields are ALWAYS read-only
  Instruction encoding fields
  Immediate value fields
Flags the issues and halts compilation
IOWarn
Examines the entire set of I/O statements in an instruction definition
Determines if the user is performing “rogue” I/O’s
Rogue I/O’s are reading/writing registers that aren’t included in the instruction format
The downstream effect is additional data paths in order to provide I/O capability to additional register files
Warns user of rogue I/O’s, but does not prevent code generation

## Slide 12: Example StoneCutter Optimization Passes
PipeBuilder
Whole ISA pipeline optimization
Examines all instruction implementations and records the set of operations required to implement the entire ISA
  I/O’s (sequential and parallel)
  Arithmetic
  Flow Control
Constructs a corollary map across instructions in order to group like operations
Required control signals are subsequently generated during code generation
**Future language support for explicit pipeline construction
test
test

## Slide 13: StoneCutter Language Specification
Language spec is governed in the same manner as source code development
  Changes to the spec must be received in the form of pull requests on Github
  Adjacent pull requests (that include all the necessary tests) must also exist in StoneCutter tree
  NO changes to the spec are accepted without support in StoneCutter
Entire language spec is documented with examples
Latest revision:
  http://www.systemarchitect.tech/index.php/stonecutter-language-spec/

## Slide 14: StoneCutter Tool Infrastructure
Tools/API Interfaces for StoneCutter

## Slide 15: StoneCutter Tool/API Infrastructure
Infrastructure/compiler implemented as a compiler linked against LLVM libs
  libSCComp
    Language frontend
    Custom passes
    Intrinsics
    Chisel code generation
Entire API interface is documented via Doxygen:
  https://codedocs.xyz/opensocsysarch/CoreGen/group__StoneCutter.html
User-facing tools include a command line interface and GUI
  Command Line: SCCOMP
  GUI: CoreGenPortal
StoneCutter Infrastructure
libsccomp
LLVM Libs
CoreGenPortal
SCCOMP
Chisel
Codegen
StoneCutter Passes
StoneCutter Parser/Lexer
StoneCutter Intrinsics
Pass
Pass
Pass
Pass
Pass
Pass
Pass
Pass
Pass
Intrin

## Slide 16: Graphical Interface: CoreGenPortal
CoreGenPortal is the primary graphical interface within System Architect
Written in C++
Graphics are handled via wxWidgets
  Currently cross platform support for Linux (Ubuntu, CentOS) and Mac OSX
Use cases
  For those seeking a development environment that resembles traditional IDE’s
  For those unfamiliar/uncomfortable with command line tools

## Slide 17: Command Line Interface: sccomp
Simple, concise command line interface to drive
  Drives compilation/optimization
Use cases:
  For those who prefer to utilize the command line and write/modify StoneCutter using text editors
  Run quick tests
  Regression/CI environments to maintain designs

## Slide 18: SCCOMP Info Options
--help : Prints the help menu
--version : Prints the version info
$> sccomp --help
$> sccomp --version

## Slide 19: SCCOMP Execution Options
Execution options require StoneCutter input input
  sscomp /path/to/input.sc
Four execution options:
  --parse : parses & optimizes the input, but does not generate Chisel
  --chisel : parses, optimizes and generates Chisel output
  --object: parse, optimizes and generates LLVM bytecode output (utilized for debugging)
  --keep: keep all the intermediate files (*.ll); combined with other execution options
$> sccomp --parse test.sc
$> sccomp --chisel test.sc
$> sccomp --object test.sc
$> sccomp --chisel --keep test.sc

## Slide 20: SCCOMP Execution Options cont.
Additional options can be utilized
--outfile /path/to/output.chisel : specifies output Chisel file
  The default is “test.sc.chisel” in the same path as the input chisel file
--optimize : enables the LLVM optimizer (enabled by default)
--no-optimize : disables the LLVM optimizer
--disable-chisel : disables the Chisel output
--verbose : Enable verbosity during compilation
$> sccomp --chisel --outfile output.chisel test.sc
$> sccomp --chisel --optimize test.sc
$> sccomp --chisel --no-optimize test.sc
$> sccomp --disable-chisel --object test.sc
$> sccomp --verbose --chisel test.sc

## Slide 21: SCCOMP Optimization Options
Users can list all the supported passes on the command line
--list-passes: prints a table of all LLVM passes
$> sccomp --list-passes

## Slide 22: SCCOMP Optimization Options cont.
Users can also enable/disable individual LLVM passes
--enable-pass “PASS1,PASS2”
--disable-pass “PASS1,PASS2”
$> sccomp --enable-pass “LICMPass” test.sc

## Slide 23: Intro to StoneCutter Syntax
Implementing Instructions in StoneCutter

## Slide 24: StoneCutter Syntax
StoneCutter is a basic, C-like language construct that is designed to provide users a rapid development tool for individual instructions
Designed to support compilation of very high level language to Chisel
Designed to support users with reasonable knowledge of hardware architecture, but not Chisel (or Verilog) HDL
Directly integrated into the remainder of the System Architect infrastructure
See slide 13 for a reference to the official StoneCutter language specification

## Slide 25: StoneCutter Syntax cont.
StoneCutter language syntax includes 10 distinct features
Comments
Datatypes
Instruction Format Definitions
Register Class Definitions
Instruction Prototypes
Variable Definitions
Arithmetic Operations
Conditional Operations
Loop Operations
Intrinsic Functions

## Slide 26: StoneCutter Syntax Notes
Semicolons: In C, expressions are terminated by semicolons (;). Semicolons are not required in StoneCutter.
Complement Operations: StoneCutter provides all the standard arithmetic, Boolean and logical operations provided by C. The one exception are complement operations (! or ~). StoneCutter does not have a native complement operations for binary or Boolean types. You must utilize the “NOT” intrinsic to complement either Boolean operations or binary operators

## Slide 27: StoneCutter Syntax: Comments
Comments can be inserted into a StoneCutter implementation on new lines or inline with the source
All comments are preceded by the ‘#’ sign
# This is a stand alone comment
def inst0( RA RB RT ){ # this is an inline comment
RT = RA + RB
}

## Slide 28: StoneCutter Syntax: Datatypes
StoneCutter supports a standard set of datatypes similar to C
Unlike C, hardware designs need the ability to support types of arbitrary width
The StoneCutter type system supports signed/unsigned types of any width {1-N bits}
u7 foo #-- unsigned 7 bit integer
u1024 bar #-- unsigned 1024 bit integer
s37 foobar #-- signed 37 bit integer

## Slide 29: StoneCutter Syntax: Instruction Format Definitions
StoneCutter requires that users define the instruction format utilized in the respective instructions
  This is analogous to C-style prototypes
Each field in the instruction format is treated as a global variable across all instruction definitions
  These globals can be read from or written to just local any global variable
Each field is designated as one of three types:
  Encoding field: enc
    Instruction encoding: Read-Only
  Immediate field: imm
    Immediate values: Read-Only
  Register Index: reg[REGCLASS]
    Register indices: Read-Write
instformat FORMATNAME( FIELDTYPE FIELD1, FIELDTYPE FIELD2, … )
Register index fields require an additional syntactical note of defining the register class that the index is associated with
  This allows us to performs I/O’s to the correct register file at the correct index
  See Register Class Definitions
Note: The field names should map back to the same naming conventions utilized in the CoreGen IR definition

## Slide 30: StoneCutter Syntax: Instruction Format Definitions cont.
Using the Arith.if format from the Level 1 tutorial, we can define our instruction format in StoneCutter
Six fields:
  Register Fields: {ra, rb, rt}
    Notice that each utilizes the GPR register file
  Encoding Fields: {opc, func}
  Immeidate Field: {imm}
instformat Arith.if(reg[GPR] ra, reg[GPR] rb, reg[GPR] rt, enc opc, enc func, imm imm)

## Slide 31: StoneCutter Syntax: Register Class Definitions
Users must also define the set of register classes contained within the design
Each register class and register is raised to a global variable across all instruction definitions
Each register must be encapsulated in a register class
Each register must include a datatype
  These are the datatypes defined in slide 28
Users can create register files with mixed data types (but performance and/or area may suffer)
Register class and register names must map back to the names defined in your CoreGen IR file
regclass RCNAME( DATATYPE RegName1, DATATYPE RegName2, … )

## Slide 32: StoneCutter Syntax: Register Class Definitions cont.
Using the GPR register file from our Level 1 tutorial, we can define a register class in StoneCutter
32 general purpose registers
All are defined as unsigned 64 bit integers
regclass GPR( u64 r0, u64 r1, u64 r2, u64 r3, u64 r4, u64 r5, u64 r6, u64 r7, u64 r8, u64 r9, u64 r10, u64 r11, u64 r12, u64 r13, u64 r14, u64 r15, u64 r16, u64 r17, u64 r18, u64 r19, u64 r20, u64 r21, u64 r22, u64 r23, u64 r24, u64 r25, u64 r26, u64 r27, u64 r28, u64 r29, u64 r30, u64 r31 )

## Slide 33: StoneCutter Syntax: Instruction Prototypes
Each instruction implementation requires an instruction definition
The instruction definition is analogous to a C-function that defines the respective implementation of the instruction
Each instruction implementation requires an instruction prototype
Prototypes provide several key implementation elements:
  Instruction naming convention that matches the decoding/instruction crack logic
  The instruction format for the instruction that provides the compiler the ability to validate the I/O structure
  The instruction arguments in the form of instruction fields, register classes or registers that define the pipelined I/O structure
def INSTNAME[:INSTFORMAT]( ARG1 ARG2 ARG3 … ){
}

## Slide 34: StoneCutter Syntax: Instruction Prototypes cont.
The INSTNAME from each instruction definition must match the complementary instruction name defined in the CoreGen IR
The INSTFORMAT is an optional syntactical addition to the instruction definition, however
  Defining the instruction format allows StoneCutter to correctly validate the I/O pipeline
  Will prevent downstream issues in creating erroneous I/O paths
  The instruction format must match an existing format defined in the instruction format block and the CoreGen IR
def INSTNAME[:INSTFORMAT]( ARG1 ARG2 ARG3 … ){
}

## Slide 35: StoneCutter Syntax: Instruction Prototypes cont.
The instruction argument list provides the set of standard I/O paths for the target function
The argument lists can include any global variables:
  Register classes
  Individual registers
  Instruction fields
Note: Most instructions will include the register and immediate fields of the respective register format
  These are things that are commonly utilized in the instruction body
Note: The instruction arguments are NOT separated by commas
def INSTNAME[:INSTFORMAT]( ARG1 ARG2 ARG3 … ){
}

## Slide 36: StoneCutter Syntax: Instruction Prototypes cont.
Using the basic ADD instruction from the Level 1 tutorial, we can define a simple prototype
Note how we define the instruction to utilize the Arith.if format and utilize the {ra,rb,rt} register fields as well as the imm field from the instruction format
def add:Arith.if( ra rb rt imm ){
#-- this is the instruction body
}

## Slide 37: StoneCutter Syntax: Variable Definitions
Variables define permanent and temporary storage for use by the instruction implementation
Variables can be global or local (just as in C)
Global variables are defined within the instruction format and register classes
Local variables are defined first in the instruction implementation body
  Just like in C where variables are defined at the top of the function
  Local variable scope is the entire instruction body
Local variables must include an associated datatype (Slide 28)
  Local variables can be initialized with specific values
  Multiple variables with the same type can be defined together
def INST:INSTFORMAT( … ) {
DATATYPE var1
DATATYPE var2 = VALUE
DATATYPE var3, var4, …
}

## Slide 38: StoneCutter Syntax: Variable Definitions cont.
Variables define permanent and temporary storage for use by the instruction implementation
Global variables reside within register file storage
Local variables generally reside within the pipeline
Note: Its imperative that you make good choices with respect to the datatypes of your local variables
  StoneCutter will always attempt to do the “right thing” with respect to the values present in the operation
  Maintaining correct datatypes for the desired operation width will ensure numerical stability
Take the following example to perform a fused multiple add operation
  **This is an incredibly simple example
  Can also be done using rt = ra + (rb * rt)
def fadd:Arith.if( ra rb rt imm ){
u64 tmp1 = 0
tmp1 = rb * rt
rt = ra + tmp1
}

## Slide 39: StoneCutter Syntax: Variable Definitions cont.
There are a number of special case global variable definitions
  Reading/writing these variables induces special backend I/O circuits
Registers: directly reading/writing named registers will directly read/write these registers within their target register files
  Registers must be defined within a register class object
Register Fields: reading/writing register fields will manipulate the register at the index referenced by the register field
  RegisterClass[Field] = Value
pc = 10 #-- set the value of the pc register to 10
rt = 15 #-- write the value 15 to the register at the index in the RT field

## Slide 40: StoneCutter Syntax: Arithmetic Operations
The StoneCutter language supports the full complement of C arithmetic operations in standard form:
  Output = Input <operator> Input
As mentioned earlier, the only exception to this is the Boolean and bitwise complement operations (!,~)
The target (output) of all operations must be writable entities (variables or register fields)
u16 tmp1 = 0
rt = ra + rb #-- legal
tmp1 = ra * rb #-- legal
imm = rt #-- ILLEGAL, “imm” is a read-only instruction field

## Slide 41: StoneCutter Syntax: Arithmetic Operations cont.
StoneCutter has a unique feature in that users can perform operations with inputs of any type
StoneCutter will attempt to up/down convert based upon the type of the output operand
Any time operations are upconverted, the extended bit space must be considered volatile. You MUST utilize the sign and zero extension intrinsics in order to maintain numerical stability
  u64 = u32 + u32
Any time operations are truncated, the least significant N bits are always taken
  u32 = u64 + u64
u64 tmp1, tmp2, tmp3
u32 tmp4, tmp5
tmp1 = tmp2 + tmp4 #-- tmp4 is extended to 64 bits
tmp4 = tmp1 + tmp3 #-- result is truncated to 32 bits (31:0)
tmp3 = tmp1 << tmp2 #-- result is still truncated to 64 bits

## Slide 42: StoneCutter Syntax: Arithmetic Operations cont.
Operator | Example | Description
= | RT = RB | Assignment operation
+ | RT = RA + RB | Add operation
- | RT = RA - RB | Subtract operation
* | RT = RA * RB | Multiplication operation
\ | RT = RA \ RB | Division operation
% | RT = RA % RB | Modulo operation
& | RT = RA & RB | Bitwise and operation
¦ | RT = RA ¦ RB | Bitwise or operation
^ | RT = RA ^ RB | Bitwise nor operation
<< | RT = RA << RB | Shift left operation
>> | RT = RA >> RB | Shift right operation

## Slide 43: StoneCutter Syntax: Conditional Operations
The StoneCutter language supports the use of conditional expressions
These conditional flow control expressions mimic traditional if-else statements in C
  The else block is optional
The expression can be any set or combination of traditional Boolean operations
The conditional operations are contained within brackets {}
if( BOOLEAN OPERATION ){
#-- Conditional Body
}
if( BOOLEAN OPERATION ){
}else{
}

## Slide 44: StoneCutter Syntax: Conditional Operations cont.
The Boolean expressions can compare any combination of local variables, global variables and immediate values
  VAR <BOOLEAN OPERATOR> VAR
Complex operations can be contained within parenthesis
Operator | Example | Description
== | RA == RB | Logical equivalence
!= | RA != RB | Logical in-equivalence
< | RA < RB | Less than
> | RA > RB | Greater than
<= | RA <= RB | Less than or equal to
>= | RA >= RB | Greater than or equal to
&& | RA && RB | Logical and
¦¦ | RA ¦¦ RB | Logical or
if( (RA >RB) && (RB < RC) || (RA == RD) ){
#-- Conditional Body
}

## Slide 45: StoneCutter Syntax: Loop Operations
StoneCutter supports a full set of for, while and do-while loop constructs
The syntax is analogous to traditional C-like loops
  Several nuances in the construction of for loops
The Boolean expressions utilized to construct the loop trips can be constructed using any Boolean operator
  See slide 44
All loop bodies are contained within brackets (mandatory)
for( looptrip = base; looptrip <BOOLEAN OPERATOR> terminator ){
}
for( looptrip = base; looptrip <BOOLEAN OPERATOR> terminator; iterator ){
}
while( Boolean expression ){
}
do{
}while( Boolean expression )

## Slide 46: StoneCutter Syntax: For Loop Operations
The for loop expression requires two statements in the loop expression with an optional third statement
Statement 1: loop trip base case
  Can be an existing variable or a new variable
  New variables will automatically be defined as new locals
Statement 2: loop termination statement
  Utilizes all the traditional Boolean operators (<,>,<=,>=)
Statement 3: optional iterator
  If iterators are not specified, then the loop is automatically assumed to add “1” to for each loop trip
  Note that the loop iterators MUST be standard arithmetic operators
  StoneCutter DOES NOT support “++”, “--”, “+=“
#-- RA, RB, RC are existing globals
for( RA = 1; RA < RB ){
#-- RA incremented by 1
}
for( RA = 20; RA > RC; RA-1 ){
#-- RA decremented by 1
}
#-- ‘i’ becomes a new local
for( i = 1; i < RB; i+1 ){
#-- i incremented by 1
}

## Slide 47: StoneCutter Syntax: While Loop Operations
The while loop expression requires one statement in the loop expression
  Loop terminator statement
While loops require that the user perform any necessary modifications to the loop trip counter within the loop body in order to avoid infinite loops
while( RA < RB ){
#-- loop body
RA = RA + 1
}

## Slide 48: StoneCutter Syntax: Do-While Loop Operations
The do-while loop expression requires one statement in the loop expression
  Loop terminator statement
Do-While loops require that the user perform any necessary modifications to the loop trip counter within the loop body in order to avoid infinite loops
do{
#-- loop body
RA = RA + 1
}while( RA < RB )

## Slide 49: StoneCutter Syntax: Intrinsic Functions
Much like other C/C++ language constructs, StoneCutter provides a set of builtin intrinsic functions
Intrinsic functions are utilized to implement pathological operations in a high performance manner
The intrinsic logic is expanded inline within the remainder of the StoneCutter source
StoneCutter intrinsics behave like function calls
  Some intrinsics have return values, several modify data in line
  Most intrinsics require arguments
  StoneCutter will perform argument checking for every included intrinsic
See Section 3 in the StoneCutter Language Spec
#-- intrinsic with a return value
RA = INTRINSIC( ARG1, ARG2, … )
#-- inline intrinsic
INTRINSIC( ARG1, ARG2, … )

## Slide 50: StoneCutter Syntax: Intrinsic Functions cont.
Two types of StoneCutter intrinsics: arithmetic and memory
Arithmetic Intrinsics
  Perform some notional permutation on the input arguments
  Returns the result of the permutation
    A = INTRIN( B )
Memory Intrinsics
  Perform loads/stores to/from memory
  Links the instruction to the memory pipeline
  Load operations return data
    A = LOAD( B )
  Store operations do not return data
    STORE( DATA, ADDR )
#-- LOAD intrinsic with a return value
RA = LOAD( ARG1 )
#-- STORE intrinsic with no return value
STORE( RA, RB )

## Slide 51: StoneCutter Syntax: Intrinsic Arguments
Unlike C-style intrinsics, StoneCutter intrinsics are typeless
Each intrinsic can accept any argument of any type or bit width
The compiler expands the intrinsic using the appropriate input/output data types with the correct internal logic
Note: Intrinsic functions are very literal! Be sure to understand how specific intrinsic functions react to certain input types. Pay special attention to the expected output type.
u8 var1 = 1234
u64 var2 = 123456789
RA = POPCOUNT( var1 )
RB = POPCOUNT( var2 )

## Slide 52: Implementing a Basic RISC Device
Implementing a basic RISC device with System Architect and StoneCutter

## Slide 53: Tutorial Source
Tutorial source is published in a Github repository
All design source code is open source under an Apache2 license
  Feel free to reuse it!!
https://github.com/opensocsysarch/CoreGenTutorials
  See the LEVEL2 subdirectory

## Slide 54: Tutorial Assumptions
Standard installation location:
  “/opt/coregen”
  EG, the “sccomp” binary will be located at /opt/coregen/bin/sccomp
  We don’t explicitly reference the fully qualified path in the tutorial
Text editing is required!
  Emacs and Vim are most prevalent, but any standard text editor will suffice
Basic command line knowledge is required
  Executing commands with arguments
Basic knowledge of Git/Github
  Only required if you seek to download/edit the tutorial content

## Slide 55: BasicRISC Core
The remainder of this Level 2 tutorial will build upon the Level 1 tutorial material
We will extend the original Level 1 design with the necessary instruction implementations
This will include all the instructions defined in our BasicRISC Core
RISC ALU
General Purpose Registers
Control Registers
Memory Interface

## Slide 56: CoreGen and StoneCutter
One of the nice features of CoreGen is the ability to directly integrate the StoneCutter syntax into the CoreGen IR design files
This allows you to inline the instruction implementation in the design
CoreGen autogenerates all the instruction format and register class blocks without user intervention
Permits users to focus on the specific instruction implementations
  Reduces the ramp to become proficient with StoneCutter
All of our work will be done in the CoreGen IR file from the Level 1 tutorial

## Slide 57: BasicRISC ISA
Traditional RISC ISA
  Opcodes (opc) determine the “class” of instructions
  Function codes (func) determine the target instruction
  Instructions are grouped by their argument types:
    INST GPR, GPR, GPR
    INST GPR, CTRL, GPR
    INST CTRL, GPR, GPR
  Plenty of opcode/function space to expand for your own use
Arithmetic:
  Integer arithmetic (2’s-complement)
  Add, Sub, Mul, Div
  Logical/Arithmetic shifts
  Logicals (AND, OR, NAND, NOR, XOR, NOT)
Comparisons:
  Compare {NE, EQ, GT, LT, GTE, LTE}
Branches
  Conditional and unconditional
  Absolute and relative (jump)
See BasicRISCInstTable for a full instruction set listing

## Slide 58: Directly Editing CoreGen Yaml IR
Yaml IR is ASCII text
Hierarchy is determined by indentions
  Indentions are SPACES, not tabs
  Each indentation should be two (2) spaces
You can use any potential editor!
A few important notes:
  Nodes are parsed in the correct order regardless of their order in the file
    We do this to preserve the natural hierarchy and dependence between nodes
  Node names are case sensitive
    “RegName” != “Regname”
  Certain nodes have required and optional attributes
    Refer to the IR documentation for what is optional
  Comments are delineated with ‘#’ characters
    Similar to BASH shell scripts
#-- this is a comment
NODE:
- SubNode: Name1
Attribute1: 64
Attribute2: false
Attribute3: This_Is_A_String
- SubNode: FOO
Bars:
- bar0
- bar1
- bar2
Example CoreGen Yaml IR Formatting

## Slide 59: Ten Design Steps for Level 2
Step 1: Copy the CoreGen Yaml IR file from the Level 1/Step 10 directory
Step 2: Update the project definition for our Level 2 directory structure
Step 3: Implement the arithmetic instructions
Step 4: Implement the comparison instructions
Step 5: Implement the load/store instructions
Step 6: Implement the logical NOT instruction
Step 7: Implement the branch instructions
Step 8: Implement the control instructions
Step 9: Compile the StoneCutter source
The CoreGen IR for each step is outlined in ~/CoreGenTutorials/LEVEL2/StepN

## Slide 60: Step 1: Copy the basic project files
The first step in the Level 2 tutorial is to copy over the CoreGen design input from Step10 of the Level1 tutorial
We will build upon the work done in the Level 1 tutorial material
~/CoreGenTutorials/LEVEL2/Step1
$> cd ~/CoreGenTutorials/LEVEL2/Step1
$> cp ../LEVEL1/Step10/BasicRISC.yaml ./

## Slide 61: Step 2: Update the project definition
With the Level 2 tutorial, we need to define the project structure
The project structure will be utilized to generate all the necessary directory structure and intermediate makefiles
Edit the BasicRISC.yaml file and specify a new ProjectRoot directory
  This will place all our generated files in the ./BasicRISC directory
~/CoreGenTutorials/LEVEL2/Step2
# -------------------------------------------------------
# ProjectInfo Section
# -------------------------------------------------------
ProjectInfo:
- ProjectName: BasicRISC
ProjectRoot: ./BasicRISC
ProjectType: soc
ChiselMajorVersion: 3
ChiselMinorVersion: 0

## Slide 62: Step 3: Implement the arithmetic instructions
In this stage of the tutorial, we will begin implementing instructions
Rather than implementing our StoneCutter source code by hand, we will utilize a unique feature of CoreGen to assist our development process
CoreGen can directly include inline StoneCutter language syntax in the design input (YAML)
  Users define the body of each instruction
  CoreGen will automatically generate all the instruction formats, register class and instruction prototypes
Each instruction block in the YAML input will require a new attribute: Impl
~/CoreGenTutorials/LEVEL2/Step3
Impl: Insert StoneCutter syntax here

## Slide 63: Step 3: Implement the arithmetic instructions
In this stage of the tutorial, we will begin implementing instructions
Rather than implementing our StoneCutter source code by hand, we will utilize a unique feature of CoreGen to assist our development process
CoreGen can directly include inline StoneCutter language syntax in the design input (YAML)
  Users define the body of each instruction
  CoreGen will automatically generate all the instruction formats, register class and instruction prototypes
Each instruction block in the YAML input will require a new attribute: Impl
  Impl attributes may include any syntactical nuances, including newlines, brackets, etc
~/CoreGenTutorials/LEVEL2/Step3
Insts:
- Inst: add
ISA: BasicRISC.ISA
InstFormat: Arith.if
Encodings:
- EncodingField: opc
EncodingWidth: 5
EncodingValue: 0
- EncodingField: func
EncodingWidth: 5
EncodingValue: 0
- EncodingField: imm
EncodingWidth: 7
EncodingValue: 0
Impl: Insert StoneCutter syntax here

## Slide 64: Step 3: Implement the arithmetic instructions cont.
~/CoreGenTutorials/LEVEL2/Step3
instformat Arith.if(reg[GPR] ra,reg[GPR] rb,reg[GPR] rt,enc opc,enc func,imm imm)
regclass GPR( u64 r0, u64 r1, u64 r2, u64 r3, u64 r4, u64 r5, u64 r6, u64 r7, u64 r8, u64 r9, u64 r10, u64 r11, u64 r12, u64 r13, u64 r14, u64 r15, u64 r16, u64 r17, u64 r18, u64 r19, u64 r20, u64 r21, u64 r22, u64 r23, u64 r24, u64 r25, u64 r26, u64 r27, u64 r28, u64 r29, u64 r30, u64 r31 )
def add( ra rb rt imm )
{
rt = ra + rb
}
Insts:
- Inst: add
ISA: BasicRISC.ISA
InstFormat: Arith.if
Encodings:
- EncodingField: opc
EncodingWidth: 5
EncodingValue: 0
- EncodingField: func
EncodingWidth: 5
EncodingValue: 0
- EncodingField: imm
EncodingWidth: 7
EncodingValue: 0
Impl: rt = ra + rb
CoreGen Design Input
Generated StoneCutter Output

## Slide 65: Step 3: Implement the arithmetic instructions cont.
Arithmetic instructions we need to implement:
~/CoreGenTutorials/LEVEL2/Step3
add: rt = ra + rb
sub: rt = ra - rb
mul: rt = ra * rb
div: rt = ra / rb
divu: rt = ra / rb
sll: rt = ra << rb
srl: rt = ra >> rb
sra: rt = ra >> rb
and: rt = ra & rb
or: rt = ra | rb
#-- note how we use intrinsics
nand: rt = NOT(ra & rb)
nor: rt = NOT(ra | rb)
xor: rt = ra ^ rb
add
sub
mul
div
divu
sll
srl
sra
and
or
nand
nor
xor

## Slide 66: Step 4: Implement the comparison instructions
Using the same technique, we need to implement our comparison instructions that utilize if/else clauses
Instructions:
  cmp.ne
  cmp.eq
  cmp.gt
  cmp.lt
  cmp.gte
  cmp.lte
~/CoreGenTutorials/LEVEL2/Step4
cmp.ne: if( ra != rb ){ rt = 2 }else{ rt = 0 }
cmp.eq: if( ra == rb ){ rt = 3 }else{ rt = 0 }
cmp.gt: if( ra > rb ){ rt = 4 }else{ rt = 0 }
cmp.lt: if( ra < rb ){ rt = 5 }else{ rt = 0 }
cmp.gte: if( ra >= rb ){ rt = 6 }else{ rt = 0 }
cmp.lte: if( ra <= rb ){ rt = 7 }else{ rt = 0 }

## Slide 67: Step 5: Implement the load/store instructions
Using the same techniques, we need to define our load/store instructions
  Note that we will utilize memory intrinsics to enable the memory pipeline
~/CoreGenTutorials/LEVEL2/Step5
lb: rt = SEXT(LOADELEM(ra+imm,8),7)
lh: rt = SEXT(LOADELEM(ra+imm,16),15)
lw: rt = SEXT(LOADELEM(ra+imm,32),31)
ld: rt = LOADELEM(ra+imm,64)
sb: STOREELEM(SEXT(ra,7),rt+imm,8)
sh: STOREELEM(SEXT(ra,15),rt+imm,16)
sw: STOREELEM(SEXT(ra,31),rt+imm,32)
sd: STOREELEM(ra,rt+imm,64)
lbu: rt = ZEXT(LOADELEM(ra+imm,8),7)
lhu: rt = ZEXT(LOADELEM(ra+imm,16),15)
lwu: rt = ZEXT(LOADELEM(ra+imm,32),31)
sbu: STOREELEM(ZEXT(ra,7),rt+imm,8)
shu: STOREELEM(ZEXT(ra,15),rt+imm,16)
swu: STOREELEM(ZEXT(ra,31),rt+imm,32)
lb
lh
lw
ld
sb
sh
sw
sd
lbu
lhu
lwu
sbu
shu
swu

## Slide 68: Step 6: Implement the logical NOT instruction
Using the same techniques, we can now implement the logical NOT instruction
  Two operand instruction
  Utilizes the NOT intrinsic to implement the only valid input argument
~/CoreGenTutorials/LEVEL2/Step6
not: rt = NOT(ra)

## Slide 69: Step 7: Implement the branch instructions
Using the same techniques, we can now implement the branch instructions
These are unique in that they utilize mixtures of explicit registers (pc, rp) as well as register inputs from the instruction payload
  We also utilize if/else expressions for conditional branches
~/CoreGenTutorials/LEVEL2/Step7
bra: pc = rt
br: pc = pc + r)
brac: if( ra == rb ){ pc = rt }else{ pc = pc + 4 }
brc: if( ra == rb ){ pc = pc + rt }else{ pc = pc + 4 }
bra
br
brac
brc

## Slide 70: Step 8: Implement the control instructions
Using the same techniques, implement our move to/from control instructions
Note that we utilize the traditional RISC method of doing so: add pipeline
Instructions
  ladd
  cadd
~/CoreGenTutorials/LEVEL2/Step8
ladd: rt = ra + rb
cadd: rt = ra + rb

## Slide 71: Step 9: Compile the StoneCutter source
Now that we have our entire ISA implementation defined, we must perform two steps to generate the Chisel output
Execute the CoreGen code generator to construct the directory structure and our master StoneCutter file
Compile the StoneCutter master implementation file
~/CoreGenTutorials/LEVEL2/Step9

## Slide 72: Step 9: Compile the StoneCutter source cont.
Ensure that the CGCLI binary is in your path
Execute the CoreGen code generator in order to generate the necessary directory structure and the master StoneCutter source file
~/CoreGenTutorials/LEVEL2/Step9
$> cgcli --chisel --ir BasicRISC.yaml
This will generate the ./BasicRISC/ directory
Your StoneCutter source file will reside in ./BasicRISC/RTL/stonecutter/BasicRISC.ISA.sc
  The file name is inherited from the name of the ISA from the YAML input

## Slide 73: Step 9: Compile the StoneCutter source cont.
Instruction Formats
Instruction Definitions
Register Classes

## Slide 74: Step 9: Compile the StoneCutter source cont.
Now that we have the full StoneCutter source, we can compile it to Chisel
Ensure that the SCCOMP binary is in your path
~/CoreGenTutorials/LEVEL2/Step9
$> sccomp --chisel ./RTL/stonecutter/BasicRISC.ISA.sc
Note: we will see some warnings from the StoneCutter compiler
  But why!?

## Slide 75: Step 9: Compile the StoneCutter source cont.
As mentioned in the intro, StoneCutter includes a set of safety and performance optimization passes
The safety passes analyze the structure of the instruction implementation in order to verify whether the implementation is safe and/or induces unwanted performance idiosyncrasies
Optimization passes modify the source in a safe manner in order to improve performance
  Both of the arithmetic pipeline and the I/O channels
~/CoreGenTutorials/LEVEL2/Step9
The warnings we saw when compiling our source come from the IOWarn pass
The IOWarn pass analyzes the use of all global variables in order to ensure that the instruction format has predefined I/O paths for the appropriate variables
  Reading/Writing registers outside of these paths will force the StoneCutter compiler to generate additional paths, which may have a negative effect on performance
The branch instructions flagged by the warning exhibit this case
  The branch instructions are of type Arith.if, which only include paths for GPR registers
  The PC register is a CTRL register, thus an additional path is generated
  Given that branches are known to be latent instructions, this is ok for our design

## Slide 76: Step 9: Compile the StoneCutter source cont.
~/CoreGenTutorials/LEVEL2/Step9
GPR Register File
CTRL Register File
Branch Logic
ALU
RA
RB
Arith.if: RT = GPR; RA = GPR; RB = GPR
RT
PC
Standard I/O Path
Additional I/O Path
The IOWarn pass detects the additional required I/O path and warns the user. This is NOT an error, just a warning

## Slide 77: References
Where do I find more info?

## Slide 78: Web Links
System Architect Public Web
  http://www.systemarchitect.tech/
Documentation
  Latest StoneCutter Specification:
    http://www.systemarchitect.tech/index.php/stonecutter-language-spec/
Tutorials
  http://www.systemarchitect.tech/index.php/tutorials/
  https://github.com/opensocsysarch/CoreGenTutorials

## Slide 79: Source Code
Main source code hosted on Github:
  https://github.com/opensocsysarch
CoreGen Infrastructure
  https://github.com/opensocsysarch/CoreGen
CoreGenPortal GUI
  https://github.com/opensocsysarch/CoreGenPortal
CoreGen IR Spec
  https://github.com/opensocsysarch/CoreGenIRSpec
StoneCutter Language Spec
  https://github.com/opensysarch/StoneCutterLanguageSpec
System Architect Weekly Development Releases
  https://github.com/opensocsysarch/SystemArchitectRelease

## Slide 80: Contact
Issues should be submitted through the respective Github issues pages (see source code links)
Mailing Lists:
  http://www.systemarchitect.tech/index.php/lists/
Direct developer contacts
  John Leidel: jleidel<at>tactcomplabs<dot>com
  David Donofrio: ddonofrio<at>tactcomplabs<dot>com
  Ryan Kabrick: rkabrick<at>tactcomplabs<dot>com